## Slide 1: THEORETICAL MECHANICS
Electronic Textbook
DOLGOV A.M.
DNIPROPETROVS’K- 2015
NMU
MINISTRY OF EDUCATION AND SCIENCE OF UKRAINE
STATE HIGHER EDUCATIONAL INSTITUTION
«NATIONAL MINING UNIVERSITY»
DEPARTMENT OF STRUCTURAL THEORETICAL AND APPLIED MECHANICS

## Slide 4
УДК 531(075.8)
ББК 22.21я73
Д 64
Затверджено вченою радою Державного вищого навчального закладу «Національний гірничий університет» як підручник для здобувачів вищої освіти за галуззю знань 14 Електрична інженерія спеціальності 141 Електроенергетика, електротехніка та електромеханіка (протокол № 14 від 20.10.15).
Рецензенти:
О.С. Бешта, член-кореспондент НАН України, д.т.н, професор, завідувач кафедри електроприводу Державного вищого навчального закладу «Національний гірничий університет»;
О.Б. Іванов, к.т.н., професор, директор інституту електроенергетики Державного вищого навчального закладу «Національний гірничий університет».
Dolgov, A.M.
Theoretical mechanics [electronic resource] : electronic textbook / A.M. Dolgov ; Ministry of Education and Science of Ukraine, National Mining University. – Dnipropetrovs'k : NMU, 2015. – 124 p.
The content of the electronic textbook corresponds to the educational and vocational training program for the applicants of higher education in the specialty 141 Electric power engineering, Electrotechnics and Electromechanics, in particular - discipline «Theoretical Mechanics». The basic notions of Statics, Kinematics and Dynamics are considered. Examples of practical problem solutions are represented.
Долгов, О.М.
Теоретична механіка [електронний ресурс] : електронний підручник / О.М. Долгов ; Міністерство освіти і науки України, Національний гірничий університет. – Дніпропетровськ : НГУ, 2015. – 124 с.
Зміст електронного підручника відповідає освітньо-професійній програмі підготовки здобувачів вищої освіти за спеціальністю 141 Електроенергетика, електротехніка та електромеханіка, зокрема – дисципліні «Теоретична механіка». Розглянуто базові питання статики, кінематики і динаміки. Наведено приклади розв’язування практичних задач.
УДК 531(075.8)
ББК 22.21я73
 О.М. Долгов, 2015
 Державний ВНЗ «Національний гірничий
університет», 2015

## Slide 5
PREFACE
The purpose of this electronic textbook is to provide the students with the theoretical background and engineering applications of Theoretical Mechanics. It is divided into three parts.
The first one - Statics, deals with the two basic problems: the composition of forces and reduction of force system to as simple a form as possible, and determination of the conditions for the equilibrium of force system acting on rigid bodies.
The second part, Kinematics provides procedures for the determination of the kinematic characteristics (velocity and acceleration) of a particle and rigid body.
The last part, Dynamics offers the relationships between motion and forces that act on bodies. It treats the general principles that can be applied to any system of particles regardless of their number and internal forces acting between the individual particles. Because each continuum (fluid, gas, rigid or elastic body) can be considered as a system of particles, the derived equations form a base for development of many branches of mechanics (fluid mechanics, solid mechanics, strength of materials etc.).
The textbook is represented in the form of sections which are given as an illustrative material. The sections are ended with their summaries. There are solutions of the problems for the main sections of the electronic manual.
Attention may be called to the arrangement in the text. This textbook is elaborated and based mainly on the following sources: 1. Бондаренко А.Н. «Курс лекций по теоретической механике. Статика, Кинематика, Динамика», Москва – 2007, www.teoretmeh.ru/Statika.ppt1, www.miit.ru/institut/ipss/faculties/trm/main.htm (illustrations and their animation are used); 2. S.M. Targ «A Short Course of Theoretical Mechanics», Foreign Languages Publishing House, Moscow.
It should be born in mind that this textbook is not a simple translation or compilation of the mentioned manuals. Its arrangement is founded upon the author's experience in teaching the subject for many years in the National Mining University (Ukraine).
With this textbook the author hopes to provide a teaching and learning experience that is not only effective but also motivates the study and application of Theoretical Mechanics for foreign students and for those who study some subjects of the curricula in English.
iv

## Slide 6
STUDY UNIT DISCRIPTION
TITLE Theoretical Mechanics
ECTS CREDITS 6
DEPARTMENT Structural, Theoretical and Applied Mechanics
LEVEL 2-nd Year in Modular Underground Course
DESCRIPTION Statics: Basic Concepts and Principles of Statics. Constraints and Their Reactions. Concurrent force System. Conditions for the Equilibrium of a Concurrent Force System. Coplanar Force System. Moment of a Force About a Point. A Force Couple. Plane Trusses. Stability of Equilibrium. Arbitrary Force System in Space. Equilibrium Equations for Arbitrary Force System. Centre of Gravity.
Kinematics: Kinematics of a Particle. Methods of Describing Motion. Velocity and Acceleration of a Particle. Some Special Cases of Particle Motion. Kinematics of a Rigid Body. Translational Motion.
Rotational Motion. Plane Motion. Resultant Motion of a Particle.
Resultant Motion of a Body.
Dynamics: Laws of Dynamics. Differential Equations of Motion for a Particle and Their Integration. Vibration of a Particle. Free Harmonic Motion. Damped Vibration. Damped Forced Vibrations. Resonance.
Dynamics of a System. Linear Momentum. Impulse of a Force. Theorem of the Motion of a Center of Mass. Theorem of the Change in Linear Momentum. Angular Momentum. Theorem of the Change in the Angular Momentum. Moment of Inertia of a Body about an Axis. Differential equation of Rotational Motion of a Body. Work Done by a Force. Power. Kinetic Energy. Theorem of the Change in the Kinetic Energy. Potential Energy of a System. Dynamics of Translational and Rotational Motion of a Rigid Body. Compound Pendulum. Dynamics of a Plane Motion of a Rigid Body. D’Alembert’s Principle. Analytical Mechanics. Generalized Coordinates. Virtual Displacements of a System. Degrees of Freedom. The Principle of Virtual Work. The General Equation of Dynamics. Generalized Forces. Lagrange’s Equations.
v

## Slide 7: Study-unit Aims: The study of Theoretical Mechanics is to develop the capacity to predict the effects of force and motion in the course of carrying out the creative design function of engineering. Learning Outcomes: 1.Knowledge & Understanding: The learner should able to Understand the nature of mechanical problem (static, kinematic or dynamic) and choose the respective method of solving; Distinguish and categories different type of static and dynamic problems; Describe the problem using appropriate concepts, principles and theorems of Theoretical Mechanics; Make up and analyze equations of equilibrium and motion of various mechanical systems; Know and apply basic theories and principles of Statics, Kinematics and Dynamics; Understand the direct relevance of problems discussed in Theoretical Mechanics and engineering practice. 2.Skills: Apply knowledge of Theoretical Mechanics to solve engineering problems; Select appropriate methods for modeling and analyzing the problems of Statics, Kinematics and Dynamics; Think in a creative and innovative way in problem solving; Investigate the failure of mechanical systems, and processes; Solve engineering problems on the basis of limited and possibly contradicting information; Create and/or re-design a mechanical process or system, and carry out specialized engineering designs; Search for information and engage in life-long self-learning discipline. Pre-requisite Study-units: Higher Mathematics, Physics, Engineering and Computer Graphics. METHOD OF ASSESSMENT: 10% Home assignments; 20% Mid-term test; 20% Oral examination; 50% Final-term examination. 100% Total.
vi

## Slide 8: THEORETICAL MECHANICS
Part I Statics

## Slide 9
Content of the part I corresponds to the educational and vocational program on Electric power engineering, Electrotechnics and Electromechanics, particularly, to the subject of Theoretical Mechanics. Notions of Statics are considered. Examples of practical problem solutions are represented.
Section 1. Introduction. Basic Concepts and Principles of Statics. Constraints and Their Reactions.
Section 2. Concurrent force System. Composition of Forces. Resultant of Concurrent Forces. Conditions for the Equilibrium of a Concurrent Force System. Equilibrium Equations.
Section 3. Coplanar Force System. Moment of a Force About a Point. A Force Couple. Moment of a Couple. Theorems of Equivalence of Couples. Principle Vector and Principle Moment. Equilibrium Conditions. Varignon's Theorem.
Section 4. Plane Trusses. Method of Joints. Ritter's Method (Method of Sections). Equilibrium of Systems of Bodies. Equilibrium Condition for Lever. Stability of Equilibrium
Section 5. Sliding Friction. Basic Laws. Angle of Friction. Cone of Friction. Equilibrium with Friction. Rolling Friction.
Section 6. Arbitrary Force System in Space. Moment of a Force About a Point and an axis. Relation between the Moments of a Force about a Centre and Axis. Couples in Space. Principle Vector and Principle Moment.
Section 7. Analytical determination of Principle Vector and Principle Moment. Equilibrium Equations for Arbitrary Force System in Space. Reduction of Three-dimensional Force System. Varignon's Theorem.
Section 8. Composition of Parallel Forces. Centre of Parallel Forces. Centre of Gravity. Methods of Determining the Location of the Centre of Gravity of Bodies. Centre of Gravity of Some Homogeneous Bodies.
REFERENCES
1. Бондаренко А.Н. “Курс лекций по теоретической механике. Статика”, Москва – 2007, www.teoretmeh.ru/Statika.ppt1.
2. S. Targ. Theoretical Mechanics. A Short Course. Moscow: Foreign Languages Publishing House, 421 p.
3. I.V. Meschersky. Collection of Problems in Theoretical Mechanics. – Moscow: The Higher School Publishing House, - 304 p.
4. A. Pytel, J. Kiusalaas. Engineering Mechanics: Statics, Third Edition, Cengage Learning ,200 ,First Stamford Place, Suite 400, Stamford, CT 06902, USA, - 601 p
viii

## Slide 10: Section 1
Introduction
Mechanics is a complex of sciences which treat of mechanical motion and mechanical interaction of rigid and deformable bodies, liquids and gases.
By motion in mechanics we mean mechanical motion, i.e., any change in the relative positions of material bodies in space which occurs in the
course of time.
Mechanical interaction between bodies is a such reciprocal action which changes or tends to change the state of motion or the shape of the bodies
involved. The science, which treats of the general laws of motion and equilibrium of material bodies and of their resulting mutual interactions,
is called theoretical, or general, mechanics.
According to the nature of the objects under study, theoretical mechanics is subdivided into: mechanics of a particle, i. e., of a body whose dimensions
can be neglected in studying its motion or equilibrium, and systems of particles; mechanics of a rigid body, i. e., a body whose deformation
can be neglected; mechanics of bodies of a variable mass; mechanics of deformable bodies; mechanics of liquids; mechanics of gases.
Mechanics
Applied Mechanics
Hydromechanics
Aeromechanics
Celestial Mechanics
Dynamics of Structures
Mechanics of a Ship
Building Mechanics
Hydrodynamics
Soil Mechanics
Strength of Materials
Machinery
Theory of and Machines
Theoretical Mechanics
Rock Mechanics
Mechanical system is a collection of material points (particles) or bodies in which the position or motion of each particle or body of the system depends on the position and motion of all the other particles or bodies. We shall thus regard a material body as a system of its particles.
A classical example of a mechanical system is the solar system, all the component bodies of which are connected by the forces of their mutual attraction.
1

## Slide 11: Section 1 (continuation – 1.2)
Theoretical Mechanics consists of three parts:
According to the nature of the problems treated, mechanics is divided into Statics, Kinematics, and Dynamics. Statics studies the forces and the conditions of equilibrium of material bodies subjected to the action of forces. Kinematics deals with the general properties of the motion of bodies. Dynamics studies the laws of motion of material bodies under the action of forces.
Statics
Kinematics
Theoretical Mechanics
Dynamics
■ The Basic Concepts of Theoretical Mechanics
Equilibrium is the state of rest of a body relative to other material bodies.
Force is a quantitative measure of the mechanical interaction of material bodies . Force is a vector quantity. Its action on a body is characterized by its magnitude, direction, and point of application.
Force system is any set of forces acting on a rigid body.
Kinematic state of a body is a state of rest or motion with invariable parameters.
A resultant is a single force capable of replacing the action of a system of forces on a rigid body.
If a force system acting on a free rigid body can be replaced by another force system without disturbing the body's initial condition of rest or motion, the two systems are said to be equivalent. If a free rigid body can remain at rest under the action of a force system, that system is said to be balanced or equivalent to zero.
■ Axioms of Statics
1. Axiom of inertia – Under the action of a balanced force system the body is in a state of rest or uniformly rectilinear motion.
2. Axiom of two forces – A free rigid body subjected to the action of two forces can be in equilibrium if, and only, if the two forces are equal in
magnitude, collinear, and opposite in direction.
3. Axiom of joining –The action of the given force system on a rigid body remains unchanged if another balanced force system is added to, or subtracted from, the original system.
2

## Slide 12
Section 1 (continuation – 1.3)
Axioms of Statics (continuation)
Corollary. The point of application of a force, acting on a rigid body, can be transferred to any other point on the line of action of
the force without altering its effect.
4. Axiom of parallelogram – Two forces applied at one point of a body have as the resultant a force applied at the same point and represented by the diagonal of a parallelogram constructed with the two given forces as its sides .
5. Axiom of action and reaction – To any action of one material body on another there is always an equal and oppositely directed reaction.
6. Axiom of solidification – If a freely deformable body subjected to the action of forces is in equilibrium, the state of equilibrium will not be disturbed if the body solidifies (becomes rigid).
Constraints and Their Reactions
A body not connected with other bodies and which from any given position can be displaced in any direction in space is called a free body.
A body whose displacement in space is restricted by other bodies either connected to or in contact with it is called a constrained body.
A constraint is anything that restricts the displacement of a given body in space.
The force, with which a constraint acts on a body thereby restricting its displacement, is called the reaction of the constraint.
Axiom of constraints: any constrained body can be treated as a free body relieved from its constraints, provided the latter are represented by their reactions.
3

## Slide 13
Section 1 (continuation – 1.4)
Constraints and their Reactions (continuation)
Types of constraints and their reactions
1. String, pinned rod
Reaction of the
string (pinned rod)
is directed along
the string (pinned rod) towards the
point of suspension.
2. Smooth surface or support
Reaction of a smooth surface or support is directed normal to both contacting surfaces at their point of contact and is applied at that point.
3. Cylindrical pin (bearing, hinge)
Reaction of the fixed pin passes through its center perpendicular to axis of the pin and has any direction.
Reaction of the fixed pin may be resolved into two components, Rx and Ry, parallel to coordinate axis.
4. Moved cylindrical pin (roller support)
In moved cylindrical pin (roller support) its axis can move along fixed plane. Thus, its reaction is normal to this fixed plane.
5. Ball - and - Socket joint, step bearing
Reaction of a ball - and – socket joint or step bearing passes through its center and has any direction in space.
Reaction of the ball - and - socket joint may be resolved into three components, Rx , Ry and Rz , parallel to coordinate axis.
6. Fixed support (rigid
clamp or embedding)
A
There are three reactions in plane fixed support: two components of the reactive force Rx and Ry , and reactive moment (couple) MA .
General guidance: The reaction of a constraint points away from the direction in which the given constraint prevents a body’s displacement.
4

## Slide 14
The science, which treats of the general laws of motion and equilibrium of material bodies, is called theoretical mechanics.
By motion we mean any change in the relative positions of material bodies in space which occurs in the course of time.
According to the nature of the problems treated, mechanics is divided into statics, kinematics, and dynamics.
Statics studies the forces and the conditions of equilibrium of material bodies subjected to the action of forces.
Kinematics deals with the general properties of the motion of bodies.
Dynamics studies the laws of motion of material bodies under the action of forces.
Equilibrium is the state of rest of a body relative to other material bodies. Statics of rigid bodies treats of two basic problems:
the composition of forces and reduction of force system to as simple a form as possible, and the determination of the conditions for the equilibrium of force system acting on rigid bodies.
If a force system acting on a free rigid body can be replaced by another force system without disturbing the body's initial condition of
rest or motion, the two systems are said to be equivalent.
If a free rigid body can remain at rest under the action of a force system, that system is said to be balanced or equivalent to zero.
A resultant is a single force capable of replacing the action of a system of forces on a rigid body. A force equal in magnitude,
collinear with, and opposite in direction to the resultant is called an equilibrant force.
A free rigid body subjected to the action of two forces can be in equilibrium if, and only, if the two forces are equal in magnitude,
collinear, and opposite in direction.
Two forces applied at one point of a body have as the resultant a force applied at the same point and represented by the diagonal of a parallelogram constructed with the two given forces as its sides.
If a freely deformable body is in equilibrium, the state of equilibrium will not be disturbed if the body solidifies.
The action of given force system on a rigid body remains unchanged if another balanced force system is added to, or subtracted from,
the original system.
5
To any action of one material body on another there is always an equal and oppositely directed reaction.
Summary of Section 1

## Slide 15
A body whose displacement in space is restricted by other bodies, either connected to or in contact with it, is called a constrained body.
We shall call a constraint anything that restricts the displacement of a given body in space.
The force, with which a constraint acts on a body thereby restricting its displacement, is called the force of reaction of the constraint, or simply the reaction of the constraint.
Any constrained body can be treated as a free body relieved from its constraints, provided the latter are represented by their reactions.
The free-body diagram (FBD) of a body is a sketch of the body showing all forces that act on it. The term free implies that all supports have been removed and replaced by the forces (reactions) that they exert on the body.
The following is the general procedure for constructing a free-body diagram:
2. All applied forces are drawn and labeled on the sketch. The weight of the body is considered to be an applied force acting at the center of gravity.
3.The support reactions are drawn and labeled on the sketch. If the sense of a reaction is unknown, it should be assumed. The solution will determine the correct sense: a positive result indicates that the assumed sense is correct, whereas a negative result means that the correct sense is opposite to the assumed sense.
4. All relevant angles and dimensions are shown on the sketch.
1. A sketch of the body is drawn assuming that all supports (surfaces of contact, supporting cables, etc.) have been removed.
6
Summary of Section 1

## Slide 16
Concurrent Force System – Forces whose lines of action intersect at one point are called concurrent.
Analysis of any system corresponds to consecutive resolution of the following three problems:
1. How can we simplify the system?
2. What is the simplest aspect of a system?
3. What are the equilibrium conditions for a system?
1. Shift all the forces along their lines of action to the point of intersection (kinematic
statement will be the same. This is corollary of the axiom of joining ).
Section 2
Add the first two forces F1 and F2 (axiom of parallelogram).
The number of forces was reduced by one.
Add the resultant R12 and the next force F3.
The number of forces fell again by one.
Repeat this operation with the next force F4.
Then there is only one force, equivalent to the original system.
.
The geometric sum of two concurrent forces is determined either by the parallelogram rule or by constructing a force triangle.
The geometrical sum of any forces can be determined by constructing a force polygon.
The quantity which is the geometric sum of all the forces of a given system is called the principal vector of the system.
2. The simplest form of a system is a force applied at the point of intersection of original forces.
Thus, the concurrent force system is reduced to a single force, its resultant.
3. Under the action of the set of mutually balanced forces a body can either be at rest or in motion.
The body will remain in equilibrium only if it was at rest before the moment when the balanced forces were applied.
For a system of concurrent forces to be in equilibrium it is necessary for the resultant of the forces to be zero.
Thus, for a system of concurrent forces to be in equilibrium it is necessary and sufficient
for the force polygon drawn with these forces to be closed.
Thus, the geometrical sum, or principal vector, of a set of forces is represented by a closing side of a force polygon constructed with the given forces as its sides
7

## Slide 17
The Theorem of Three Forces: if a free rigid body remains in equilibrium under the action of three
nonparallel coplanar forces, their lines of action intersect at one point.
Section 2 (continuation – 2.2)
The theorem is effective for direct determining one of two body’s reactions.
The reaction of the roller support RB is vertical (perpendicular to the fixed support).
The direction of the reaction of a fixed pin A, RA , is not immediately apparent.
If a body is in equilibrium under the action of three forces F, RA and RB,
their lines of action intersect at one point C .
The effective directions and magnitudes of reactions may be defined by the construction of the triangle and by using similarity of triangles.
The projection of the vector of a sum on an axis is equal to the algebraic sum
of the projections of the component vectors on the same axis.
Rearranging yields
Whence, projections
of the resultant are
The resultant modulus is
Direction cosines
of the resultant are
Equations for the concurrent force system
Equilibrium condition
The resultant equals zero
Whence, equilibrium
equations are
8

## Slide 18: Section 3
Coplanar Force System – forces lie in one plane and their lines of action don’t intersect in one point.
Introduce additional new notions:
Moment of Force about a Point.
A Force Couple. Moment of a Couple.
A force couple is a system of two parallel forces of the same magnitude and opposite sense.
A force couple hasn’t a resultant. It cant be simplified and replaced by one force.
The moment of a couple is defined as a quantity equal to the product of the magnitude of one of the forces
of the couple and the perpendicular distance between the forces, taken with the appropriate sign.
The moment of a couple is said to be positive if the action of the couple tends to turn a body counterclockwise, and negative if clockwise. The perpendicular distance between the lines of action of the forces is called the arm of the couple.
The algebraic sum of the moments of the forces of a couple about any point in its plane of action is independent on the location of that point and is equal to the moment of the couple.
The moment of a couple is equal to the moment of one of its forces about the point of application of the other force.
A
A
Theorems about Couples
1) A couple can be replaced by any other couple of the same moment lying in the same plane without altering the external effect.
2) The external effect of a couple on a rigid body remains the same if the couple is transferred from a given plane into any other parallel plane.
It follows from the first of these theorems two properties:
-a couple can be transferred anywhere in its plane of action;
-it is possible to change the magnitudes of the forces of a couple or its arm arbitrarily without changing its moments.
Composition of Couples in a Plane – a system of coplanar couples is equivalent to a single couple lying in the same plane the moment of which equals the algebraic sum of the moments of the component couples.
Equilibrium Condition of Coplanar Couples
9

## Slide 19: Section 3 (continuation – 3.2)
Theorem: A force acting on a rigid body can be moved parallel to its line of action to any point of the body, if we add a couple of a moment equal to the moment of the force about the point to which it is translated.
A
Consider a force F. Add at the point A two forces equal in magnitude, directed along the same line
in opposite sense, parallel and equal to the given force.
The kinematic state will not change (Axiom of joining ).
Sometimes a couple is depicted by arc arrow.
A
A
Thus, any system of coplanar forces can be reduced to an arbitrary center in such a way that it is replaced by a single force equal to the principal vector of the system and applied at the center of reduction and a single couple of moment equal to the principal moment of the system about center of reduction.
- principle vector,
-principle moment.
For any given coplanar force system to be in equilibrium it is necessary and sufficient for the following two conditions to be satisfied simultaneously
Equilibrium Equations (The first form) can be obtained by making use of these conditions and expressions for projections of a principal vector.
Hence, for any given coplanar force system to be in equilibrium it is necessary and sufficient for the sums of the projections of all the forces on each of the two coordinate axes and the sum of the moments of all the forces about any point in the plane to be separately zero.
10

## Slide 20
Section 3 (continuation – 3.3)
Varignon's Theorem. If a force system has a resultant then the moment of this resultant about any point equals algebraic sum of the moments of all forces of a system about this point.
Proof: Let a force system F1, F2, F3 … have a resultant applied at point O.
A
O
Such a system isn't in equilibrium (R ≠ 0). Balance this system with a force , equal to the
resultant R, directed along its line of action in opposite sense (axiom of two forces).
Therefore, the system of forces F1, F2, F3 … and resultant is in equilibrium and must satisfy
equilibrium equation:
Since =-R and directed along the same line, then MA() = - MA(R). Substitution of this
equality into equation yields
or
Examples of the theorem application
1. Determination of a moment about some point when it is difficult to calculate an arm of a force.
A
Resolve a force F into components F1 and F2. Then the moment of a force F about the point A may be calculated as a sum of the moments of each force about this point
2. Proof of the necessity of restrictions for the II and III form of equilibrium equations.
If , then the system is reduced to a resultant. It passes through the point A, since its moment about this point must be zero (Varignon's Theorem).
But if , the resultant has to pass through the point B as well.
A
B
Then the projection of a resultant on an axis perpendicular to AB, and the moment of a resultant about any point on AB, will be identically equals zero at any value of a resultant.
С
11

## Slide 21
Section 4
A truss is a structure that is made of straight, slender bars that are joined together to form a pattern of triangles. Trusses are usually designed to transmit forces. Consider plane trusses.
Joints – points of intersection of the members .
The members are usually riveted or welded to a plate, called a gusset plate.
Ties – vertical members.
Diagonals - inclined members.
Span – distance between supports (l).
Truss panel length - distance between ties (d).
A
B
h
l
d
The analysis of trusses is based on the following three assumptions:
1. The weights of the members are negligible. A truss can be classified as a
lightweight structure, meaning that the weights of its members are generally much smaller than the loads that it is designed to carry.
2. All joints are pins.
3. The applied forces act at the joints.
Therefore, each member of a truss is a two-force body. In a two-force body, engineers
commonly distinguish between tension and compression.
■ Method of Joints. When using the method of joints to calculate the forces in the members of
a truss the equilibrium equations are applied to individual joints (or pins) of the truss.
Because the members are two-force bodies, the forces in the FBD of a joint are concurrent.
Consequently, two independent equilibrium equations are available for each joint.
2. Designate the joints of the truss. Reactions of the members are designated by two subscripts. The subscripts
identify the member.
3. Cut out the joint A (there are two forces in this joint) and replace the action of the cut (discarded) joints by
forces (reactions) SA1 and SA6.
1
2
3
4
5
6
7
8
A
4. Make up equilibrium equation for joint A and calculate forces SA1 and SA6. Note that we have assumed the
forces in the members to be tensile. If the solution yields a negative value for a force, the force is compressive.
5. Cut out the joint 1 (there are two forces in this joint) and replace the action of the cut (discarded) joints by
forces (reactions) S1A, S12 and S16.
1
6. Make up equilibrium equation for joint 1 and calculate S12 and S16 . Forces S1A and SA1 are equal in magnitude
( axiom of action and reaction).
Sequence of calculation
1. Consider a truss as a whole body and determine reactions of supports.
Further the process is repeated in defined
order, for example: 2, 6, 7, 3, 4, 8, 5.
The cutting of the last joint B can be used as a verification of the calculation accuracy.
12

## Slide 22
Section 4 (continuation – 4.2)
A truss analysis by the method of joints is based on the FBDs of individual joints. Calculation of a force in some member demands analysis
of several joints and solution of equilibrium equations for these joints. Moreover, successive calculations can lead to accumulation of mistakes.
■ Method of Sections (Ritter's Method). Analyzing the free-body diagram of a part of a truss that contains two or more joints is called
the method of sections. The FBD for a single joint results in a concurrent, coplanar force system (two independent equilibrium equations).
When applying the method of sections, the force system will generally be non concurrent, coplanar (three independent equilibrium equations).
This method is based on working out only one equilibrium equation and using the II or III form of equilibrium conditions for a coplanar force system.
Sequence of calculation
1. Consider a truss as a single whole and determine reactions of supports.
A
B
h
l
d
1
2
3
4
5
6
7
8
2. Select the part of the truss to be analyzed. Draw section trough the truss in such way that there
will be no more than three members in this section (one of these members is to be calculated),
for example section I-I for determining S23.
I
I
3. Having isolated the one part of the truss, for example the right-hand, we discard
another part, for example the left one.
4. The action of the discarded part on another portion of the truss is replaced by reactions of
the members – S32, S36 and S76 (we have assumed the members to be in tension).
5. In order to determine unknown force S32 find Ritter's point location. This is a point of intersection
of two other forces S36 and S76. The Ritter's point for the force S32 coincides with the joint 6.
6. Considering the moment equation of all forces for the right portion of the truss about Ritter's point (joint 6),
determine unknown force S32.
7. In order to determine the unknown force S76 find Ritter's point location. This is a point of
Intersection of two forces - S32 and S36. The Ritter's point for the force S76 coincides with the
joint 3.
8. Considering moment equation of all forces for the right portion of the truss about Ritter's point (joint 3),
determine unknown force S76.
7. In order to determine force S36 consider equation of projections on a vertical axis
(Ritter's point is in infinity).
In order to determine other forces draw another section (item 2) and repeat steps described in items 3-7.
13

## Slide 23
Section 4 (continuation – 4.3)
■ Equilibrium of Systems of Bodies. In many cases the static solution of engineering structures is reduced to an investigation of systems
of connected bodies (beams, trusses). The number of unknown constraints may be greater then the number of equilibrium equations for a given mechanical structure. If the number of unknown quantities is greater than the number of equilibrium equations, the problem is statically indeterminate. A degree of static Indeterminateness for a plane is
where B – number of solid bodies, F - number of fixed supports (rigid clamps), P - number of cylindrical pins, MP - number of moved cylindrical pins.
A
B
1. Select the whole structure.
С
Only statically determinate problems (n = 0) are considered in statics.
2. Remove constraints and replace them by their reactions.
3. The number of unknown reactions is 4, the number of independent equations is 3.
It means that the structure must be divided into two separate parts. The action
of a pin C is replaced by its reactions.
4. The number of unknown reactions equals 8, the number of independent equations
for both parts is 3·2 = 6. The reactions of the internal constraint (pin C) will constitute
pairs of forces equal in magnitude and opposite in sense in accordance
with the axiom of action and reaction . Hence, we have six unknown reactions.
5. Write six equations of equilibrium: three equations for the left-hand part of the structure (AC), and three for the right part (BC). Solving the system of six equations we can determine all six unknown quantities.
■ Equilibrium of Lever. Lever – solid body with one fixed point. For a plane case it has one degree of freedom
(w = – n = 3B – 3F – 2P – MP = 3·1 – 3·0 – 2·1 – 0 = 1). It can be in equilibrium only at certain active forces.
A
■ Equilibrium Equations for Lever.
In many cases the calculation of reactions is not the objective, and the ratio of the given forces is determined from the last equation, which is called the equilibrium equation for a lever.
Equilibrium equations for lever is used in breast wall calculating and in load overturning.
A
Overturning Stability Condition. A retentive moment of a force F1 about fixed point (A) is to be greater then
the overturning moment of a force F2 about the same point.
14

## Slide 24
The moment of a force about a center is the product of the force magnitude and the length of the moment arm taken with appropriate sign.
The perpendicular distance from the point to the line of action of a force is called the moment arm of this force about the center.
The moment of a force does not change if the point of application of the force is transferred along its line of action.
A force couple is a system of two parallel forces of the same magnitude and opposite sense.
The moment of a couple is defined as a quantity equal to the product of the magnitude of one of the forces of the couple and the perpendicular distance between the forces, taken with the appropriate sign.
A couple can be replaced by any other couple of the same moment lying in the same plane without altering the external effect.
A force system constituting a couple is not in equilibrium.
15
Summary of Sections 3-4
The external effect of a couple on a rigid body remains the same if the couple is transferred from a given plane into any other parallel plane.
The algebraic sum of the moments of the forces of a couple about any point in its plane of action is independent of the location of that point and is equal to the moment of the couple.
A system of coplanar couples is equivalent to a single couple lying in the same plane the moment of which equals the algebraic sum of the moments of the component couples.

## Slide 25
For a coplanar system of couples to be in equilibrium it is necessary and sufficient for the algebraic sum of their moments to be zero.
Force acting on a rigid body can be moved parallel to its line of action to any point of the body, if we add a couple of a moment equal to the moment of the force about the point to which it is translated.
The geometrical sum of all the forces of the given system is called the principal vector of the system.
The sum of the moments of all the forces of the system about some center is called the principal moment of the force system about
this center.
Any system of coplanar forces can be reduced to an arbitrary center in such a way that it is replaced by a single force equal to the principal vector of the system and applied at the center of reduction and a single couple of the moment equal to the principal moment of the system about a center of reduction.
For any given coplanar force system to be in equilibrium it is necessary and sufficient for the sums of the projections of all the forces on each of the two coordinate axes and the sum of the moments of all the forces about any point in the plane to be separately zero.
For any given coplanar force system to be in equilibrium it is necessary and sufficient for the sums of the moment of all the forces about any three non-collinear points to be zero.
The moment of the resultant of coplanar forces about any center is equal to the algebraic sum of the moments of the component forces about that center.
For any given coplanar force system to be in equilibrium it is necessary and sufficient for the sums of the moments of all the forces about any two points and the sum of the projections of all the forces on any axis not perpendicular to the straight line connecting these point to be separately zero.
16
Summary of Sections 3-4
Problems in which the number of unknown reactions is greater than the number of equilibrium equations are called statically indeterminate, and the corresponding systems of bodies are called statically indeterminate. The difference between the number of unknown quantities and the number of equilibrium equations is called a degree of the static indeterminateness.

## Slide 26
Section 5
■ Sliding Friction. When two bodies tend to slide on each other, a resisting force appears at their surface of contact which opposes their relative motion. This force is called sliding friction.
The laws of sliding friction can be formulated as follows:
When two bodies tend to slide on each other, a frictional force is developed at the surface of contact, the magnitude of which can have any value from zero to a maximum value which is called limiting friction
The limiting friction is equal in magnitude to the product of the coefficient of static friction (or friction of rest) and the normal pressure or normal reaction.
3. The coefficient of static friction f is a dimensionless quantity which is determined experimentally and depends on the material of the contacting bodies and the conditions of their surfaces.
4. Within broad limits, the value of limiting friction does not depend on the area of the surface of contact.
Methods of the Friction Coefficient Testing.
1. Shear force changes from zero to its maximum 0 ≤ T ≤ Tmax, (0 ≤ P ≤ Pmax).
2. Normal pressure changes from some initial value to minimal value N0 ≥ N ≥ Nmin (G0 ≥ G ≥ Gmin).
3. Shear force and normal pressure change when the angle of the plane inclination changes from zero to maximum: 0 φ φmax .
Active forces (G, T at alias) can be replaced by resultant P (it is not shown), which has the deviation angle α. It can be shown that the state of equilibrium is possible only if this force is within the cone of friction.
Equilibrium condition along x-axis Psinα ≤ Ffrmax.
From equilibrium equation along y-axis N = Pcosα.
Maximum force of friction Ffrmax = fN = tgφN = tgφPcosα.
Then Psinα ≤ tgφPcosα, whence tgα ≤ tgφ or α ≤ φ.
17

## Slide 27
Section 5 (continuation – 5.2)
■ Equilibrium with friction. The problems usually are limited by considering conditions when the motion is impending. We add forces of friction to the active forces and reactions of absolutely smooth supports. The known equilibrium equations are then written taking into account that the frictional forces acquire their maximum values (friction of impending motion).
1. Choose the object (man and ladder), remove constraints (supports) and replace them by reactions of smooth support.
A
B
2. Add active forces ( force of weight G).
3. Add forces of friction at points A and B of the ladder which are opposite in direction to the force which tend to move a ladder.
4. Write equilibrium equations
5. Add expressions
for forces of friction
6. Substitution of these expressions into equilibrium equations and simple transformations yields
7. Solution of the first two equations yields normal reactions
8. Substitution of the equations for normal reactions into the third equilibrium equation makes it possible to find the limiting
inclination angle α
■ Determination of the equilibrium band. The problem is solved for the specific man's location,
angle of inclination corresponds to the impending motion (limiting forces of friction are used).
Define the man's possible equilibrium band on the ladder by making use of the notion of the angle of
friction, formed by the rough surface, and the theorem of three forces.
It is sufficient (taking into account coefficients of friction) to determine angles of friction, which define the
limiting positions of the complete reactions, and draw the cones of friction. The total area of the cones
defines man's equilibrium band. It is obvious that for the man's higher location it is necessary to decrease
the angle of inclination.
A
B
18

## Slide 28
Section 5 (continuation 5.3)
The Basic Laws of Rolling Friction
1. A moment of resistance to rolling is always opposite in direction to the forces which tend to turn a roller.
2. A moment of resistance to rolling changes from zero to its maximum value
3. A maximal moment of resistance to rolling is proportional to the coefficient of rolling friction and the
normal pressure or normal reaction
4. For the given bodies in contact the coefficient of rolling friction is constant (fк = const).
19

## Slide 29
When two bodies tend to slide on each other, a frictional force is developed at the surface of contact, the magnitude of which can have any value from zero to a maximum value which is called limiting friction.
Limiting of sliding friction is equal in magnitude to the product of the coefficient of static friction (or friction of rest) and the normal pressure or normal reaction.
The coefficient of static friction is a dimensionless quantity which is determined experimentally and depends on the material of the contacting bodies and the conditions of their surfaces.
Within broad limits, the value of limiting friction does not depend on the area of the surface of contact.
When a system is in equilibrium, a resultant reaction passes anywhere within the angle of friction (cone of friction) depending on the applied forces.
A rolling friction is defined as the resistance offered by a surface to a body rolling on it.
A moment of resistance to rolling changes from zero to its maximum value.
A maximal moment of resistance to rolling is proportional to the coefficient of rolling friction and the normal pressure or normal reaction.
A moment of resistance to rolling is always opposite in direction to the forces which tend to turn a roller.
.
20
For the given bodies in contact coefficient of rolling friction is constant.
.
Summary of Section 5

## Slide 30
Section 6
Arbitrary Force System in Space – forces are not coplanar and their lines of action don’t intersect in one point.
Elaborate some of the concepts introduced before:
Vector Expression of the Moment of a Force about a Centre.
Moment of a Force With Respect to an Axis.
Vector Expression of the Moment of a Couple.
21

## Slide 31
Moment of Couples in Space. The action of a couple on a body is characterized by the magnitude
of the couple's moment, the aspect of the plane of action, and the sense of rotation in that plane.
The moment of a couple is denoted by a vector whose modulus is equal to the magnitude of the couple's moment, normal to the plane of action in the direction from which the rotation would be observed as counterclockwise
Theorems for Couples In Space.
Translation of a couple – The external effect of a couple on a rigid body remains the same if the couple is transferred from a given plane into any other parallel plane.
Equivalence of couples – a couple can be replaced by any other couple of the same moment.
Composition of couples in space – any system of couples acting on a rigid body is equivalent to a single couple with a moment equal to the geometrical sum of the moments of the component couples.
Conditions of the couple's equilibrium
Section 6 (continuation – 6.2)
Consider the next three basic problems:
1. How can one simplify the force system?
2. What is the simplest form of a system?
3. What are the equilibrium conditions of a system?
A
A
Any system of forces can be reduced to an arbitrary center and replaced by a single force, equal to the principal vector of the system applied at the center of reduction, and a couple with a moment, equal to the principal moment of the system with respect to this center
- principle vector,
- principle moment.
22

## Slide 32
Hence, we have six equilibrium equations
Section 7
whence the
projections
of the principle
vector are
Module of the
principle vector
Direction cosines
of the principle
vector
Analytical Determination of the Principle Moment. By using its projections on coordinate axis
whence the
projections of the
principle moment
Module of the
principle moment
Direction cosines
of the principle
moment
The cases of
reduction of the
spatial force system
 |  |  | Additional condition | The simplest form of a system
1 |  |  |  | Equilibrium conditions
2 |  |  |  | Resultant
3 |  |  |  | A force couple
4 |  |  |  | Resultant
 |  |  |  | Force-and-couple (wrench)
Condition of the System Reduction to a Resultant
In analytical (coordinate) form
23

## Slide 33
Section 7 (continuation – 7.2)
Thus, the necessary and sufficient conditions for the equilibrium of any force system in space are that the sums of the projections of all the forces on each of three coordinate axes and the sums of the moments of all the forces about those axes must separately vanish.
The first three of the equations express the conditions necessary for the body to have no translational motion parallel to the
coordinate axes. The latter three equations express the conditions of no rotation about the axes.
Hence, the necessary and sufficient conditions for the equilibrium of a system of parallel forces in space are that the sum of the projections
of all the forces on the coordinate axis parallel to the forces and the sums of the moments of all the forces about the other two coordinate
axes must separately vanish.
24

## Slide 34
Section 7 (continuation – 7.3)
Proof: Let there be acting on a rigid body a force system F1, F2, F3 …Fn which can be reduced to a resultant R
applied at some point O.
This system isn't in equilibrium (R ≠ 0).
A
O
Let us apply at this point an equilibrant force -R (axiom of two forces ).
The given force system F1, F2, F3 … and now equilibrant force -R will be in equilibrium and will satisfy
all equilibrium conditions, in particular
Since a force R’ is equal to the resultant R , directed along the same line and has
opposite sense MA( -R ) = - MA(R). Substituting this expression in the previous equation,
we find
or
Projecting this vector equation on any axis we get
25
Varignon's Theorem
If a given force system has a resultant,
- the moment of that resultant with respect to any center is equal to the geometrical sum of the moments of the component forces with respect to the same center;
- the moment of that resultant with respect to any axis is equal to the algebraic sum of the moments of the component forces with respect to the same axis.

## Slide 35
The moment of a force about a center is equal to the vector product of the radius vector from the center to the point of application of the force, and the force itself.
The moment of a force about an axis is an algebraic quantity equal to the moment of the projection of that force on a plane normal to the axis with respect to the point of intersection of the axis and the plane.
The moment of a force with respect to an axis is zero if the force and the axis are coplanar.
The moment of a force with respect to an axis is equal to the projection on that axis of the vector denoting the moment of that force with respect to any point on the given axis.
Any system of couples acting on a rigid body is equivalent to a single couple with a moment equal to the geometrical sum of the moments of the component couples.
For a spatial system of couples to be in equilibrium it is necessary and sufficient for the geometric sum of their moments to be zero.
The necessary and sufficient conditions for the equilibrium of any force system in space are that the sums of the projections of all the forces on each of three coordinate axes and the sums of the moments of all the forces about those axes must separately vanish.
Any system of forces can be reduced to an arbitrary center and replaced by a single force, equal to the principal vector of the system applied at the center of reduction, and a couple with a moment, equal to the principal moment of the system with respect to this center.
.
26
Summary of Section 7

## Slide 36
Section 8
Composition of Parallel Forces. It can proved the following two theorems: 1) the resultant of two parallel forces of the same sense is equal to the sum of their magnitudes, parallel to them, and is of same sense; the line of action of the resultant is between the points of application of the component forces, its distances from the points being inversely proportional to the magnitudes of the forces.
2) the resultant of two parallel forces of opposite sense is equal in magnitude to the difference between their magnitudes, parallel to them, and has the same sense as the greater force; the line of action of the resultant lies on the extension of the line segment connecting the points of application of the component forces, its distances from the points being inversely proportional to the forces.
By adding pairwise all the forces we obtain one force, the resultant R:
If the given forces are rotated through the same angle and added, we obtain the resultant of the same magnitude but differently directed. The line of action of a resultant of parallel forces always passes through a certain point, regardless of the direction of the forces.
The point, through which the line of action of the resultant of a system of parallel forces passes, no matter how those forces are rotated about their points of application through the same angle in the same direction, is called the center of parallel forces.
С
In order to determine the location of the center of parallel forces use the Varignon's Theorem
or
A
All forces can be represented as the product of their magnitudes and unit vector e parallel to the forces
and
Then the previous formula will be , or by rearranging
From the last equation we have or
We thus obtain the following equations which specify the coordinates of the center of parallel forces:
Center of gravity of a body is a point through which the resultant of the gravity forces acting on the particles of the body passes, regardless of how the body is oriented in space.
We use the following assumptions:
1 A body is very small as compared with the earth's radius and the gravity forces of its particles may be regarded as parallel to each other.
2. A free fall acceleration is constant g = const.
3. A body is homogeneous and solid.
Taking into account these assumptions for the location of the center of gravity one can use formulas for the center of parallel forces
where ∆are the forces of gravity of the elemental volumes.
27

## Slide 37
Section 8 (continuation – 8.2)
Determining the Location of the Center of Gravity of Bodies. Divide a body into infinitesimal elements dV = dxdydz. The weight of this volume is dG =dV, where  =const – specific weight. Replace summations of discrete forces of weight Gi by integrals over volume of a body, for instants
Similarly for an area of the constant thickness (H =const ), dV = Hdxdy = HdS.
For all three coordinates we have the similar equations
For a liner body (curve) of the constant transverse section (S = const,
axis is a plane curve), dV = SdL.
Center of Gravity of Some Homogeneous Bodies.
Rectangular Area: dS=bdy.
x
x
Triangular Area:
Circular Sector:
28

## Slide 38
Section 8 (continuation – 8.3)
Methods of Determining the Location of the Center of Gravity of Bodies.
1. Method of Division. A body is divided into finite elements, for each of which the center of gravity is known.
1
2
2. Method of Supplementation. This method is a special case of the method of
division and it is used to locate the centers of gravity of bodies with holes or cavities
taking the areas of the latters with a negative sign.
1
2
3. Method of Symmetry. By virtue of the properties of symmetry, the center of gravity of homogeneous
bodies is coincident with their center of symmetry.
4. Method of Integration. See the previous examples.
5. Experimental Method (The Method of Suspension). The center of gravity of composite non-homogeneous body can be determined experimentally. In the method of suspension the body is suspended by strings attached to different points. The direction of the string supporting the body will each time give the direction of gravitational force. The point of intersection of these directions locates the center of gravity of the body.
29

## Slide 39
The resultant of two parallel forces of the same sense is equal to the sum of their magnitudes, parallel to them, and is of the same sense; the line of action of the resultant is between the points of application of the component forces, its distances from the points being inversely proportional to the magnitudes of the forces.
The resultant of two parallel forces of opposite sense is equal in magnitude to the difference between their magnitudes, parallel to them, and has the same sense as the greater force; the line of action of the resultant lies on the extension of the line segment connecting the points of application of the component forces, its distances from the points being inversely proportional to the forces.
Summary of Section 8
The point, through which the action line of the resultant of a system of parallel forces passes, no matter how those forces are rotated about their points of application through the same angle in the same direction, is called the center of parallel forces.
Center of gravity of a body is a point through which the resultant of the gravity forces acting on the particles of the body passes, regardless of how the body is oriented in space.
There exist five methods for determining the location of the center of gravity:
Method of Division;
Method of Supplementation;
Method of Symmetry;
Method of Integration;
Experimental Method (The Method of Suspension).
30

## Slide 40: THEORETICAL MECHANICS
Part II Kinematics

## Slide 41: Content of the part II corresponds to the educational and vocational program on Electric power engineering, Electrotechnics and Electromechanics, particularly, to the subject of Theoretical Mechanics. Notions of Kinematics are considered. Examples of practical problem solutions are represented.
Section 1. Kinematic of Particle. Methods of Describing Motion of a Particle. Equation of Motion. Path. Velocity of a Particle. Acceleration of a Particle. Uniformly Variable Motion. Some Special Cases of Particle Motion.
Section 2. Kinematics of a Rigid Body. Kinds of Motion. Translational Motion.
Rotational Motion. Angular Velocity and Angular Acceleration. Uniformly Variable Rotational Motion. Velocities and Accelerations of the Points of a Rotating Body. Vector Representation of the Velocity and Acceleration of a Point in Rotational Motion. Euler's Formula. Transformation of Rotational Motions.
Section 3. Plane Motion of a Rigid Body. Resolution of the Plane Motion into Translation and Rotation. Equations of Plane Motion. Determination of the Velocity of a Point of a Body. Instantaneous Centre of Zero Velocity.
Section 4. Determination of the Velocity of a Point of a Body Using the Instantaneous Centre of Zero Velocity. Determination of the Acceleration of a Point of a Body.
Section 5. Resultant Motion of a Particle. Composition of Velocities in Resultant Motion. Coriolis Theorem. Coriolis Acceleration.
Section 6. Resultant Motion of a Body. Composition of Translations. Composition of Rotations. Composition of Translation and Rotation.
REFERENCES
Бондаренко А.Н. «Курс лекций по теоретической механике. Кинематика», Москва – 2007, www.miit.ru/institut/ipss/faculties/trm/main.htm
Targ. Theoretical Mechanics. A Short Course. Moscow: Foreign Languages Publishing House, 421 p.
3. I.V. Meschersky. Collection of Problems in Theoretical Mechanics. – Moscow: The Higher School Publishing House, - 304 p.
4. A. Pytel, J. Kiusalaas. Engineering Mechanics: Dynamics, Third Edition, Cengage Learning, 200, First Stamford Place, Suite 400, Stamford, CT 06902, USA, - 673 p.
ii

## Slide 42: Section 1
Kinematics of a Particle. Kinematics is a part of mechanics which treats of
the geometrical aspects of the bodies’ motion, without taking into account their
inertia, i.e., mass or the forces acting on them.
By motion in Kinematics is meant the relative displacement
with time of a body in space with respect to other bodies.
We start the study of Kinematics with an investigation of the
simplest object - a particle, proceeding later to the examination of the Kinematics of rigid body.
To describe the motion of a given body means to specify the position of that body relative to a given frame of reference for any moment of time.
The continuous curve described by a particle moving with respect to a given frame of reference is called the path of that particle.
Kinematics of a Particle
Kinematics
Kinematics of a Rigid Body
M
O
Coordinates of a particle are given.
M
O
The law of the motion and a path are given.
M
O
There are three methods of describing motion of a particle:
Vector method Coordinate method Natural method
The magnitude and direction of the radius vector are given.
These methods are equivalent and related.
1. Vector and coordinate method – by equation
2. Coordinate and natural method – by equation
dy
3. To obtain the equation of the path of a particle in their coordinates time t must be eliminated from the equations of motion.
The last two equations represent equations of surfaces whose line
of intersection is the path of a particle.
Example
The last two equations represent equations of the cylindrical surface of the radius R with
generatrix parallel to the axis z and a plane parallel to the plane Oxy which is shifted along
the axis z by c. The line of intersection of these surfaces (circumference of the radius R) is
a path of the particle.
1

## Slide 43: Section 1 (continuation – 1.2)
Velocity of a particle characterizes the time rate of change of its displacement in magnitude and direction.
Three methods of describing motion define the methods of determining velocity.
Vector method. Consider a location of the particle at two instants t and t1= t + t.
M
O
M1
The average velocity of the particle during the given time interval ∆t is directed along the secant MM1.
The vector of instantaneous velocity of a particle is equal to the first derivative of the radius vector of the particle with respect to time. As the limiting direction of the secant MM1 is a tangent, the vector of instantaneous velocity is tangent to the path of the particle in the direction of motion.
Consider the limit at t  0.
.
Coordinate method. The radius-vector of a particle is
M
O
Projections
of the velocity
on coordinate
axis
Natural method. Consider the radius-vector as a combined function
M
O
Derivative of the
radius-vector is
M1
The limiting position of the increase in velocity in the time interval ∆t is a tangent to the path of the particle.
Thus, the derivative of the radius-vector with respect to the arc coordinate is a unit vector directed along the tangent to the path.
The velocity vector is The tangent projection of the velocity is
At the velocity is directed towards the increase of the arc coordinate, otherwise – in the opposite direction.
The first derivative of the radius-vector with respect to the arc coordinate is 1.
By using vector method of determining velocity we obtain
Use vector method of the velocity determination
Components
of the velocity
vector
2

## Slide 44: Section 1 (continuation – 1.3)
Acceleration characterizes the time rate of change of velocity in magnitude and direction.
Three methods of describing motion define the methods of determining acceleration.
Vector method: Consider location of the particle at two instants t and t1= t + t
M
O
M1
M2
The average acceleration of the particle during the given time interval ∆t is directed towards the inside of the path.
Consider the limit at t  0
In general case, the acceleration vector lies in the osculating plane and is directed towards the inside of the curve. The osculating plane trough a point M on a curve may be defined as the limiting position of a plane trough points M, M1 and M2 of the given curve when points M1 and M2 tend to M.
Coordinate method. The radius-vector of a particle is
M
O
Projections
of the
acceleration
on coordinate
axis
Components
of the
acceleration
vector
Natural method. Use the vector expression of the acceleration and formula for the vector velocity in natural method of describing motion
M
O
M1
The first derivative of the
unit tangent vector with respect to the arc coordinate
Let us fined the tangent unit vector as a combined function
The first derivative of the
unit tangent vector
At s  0 radius of the curvature 1  , angle
between radii of the curvature   0, nominator
is a base of the isosceles triangle with sides 1
and , denominator – length of the arc of the radius .
The angle between the
increment of the unit vector
 and vector  tends to 90о
at   0.
Consider the unit vector n, normal (perpendicular) to the tangent towards the center of the curvature.
By using vector n and the values determined earlier
the acceleration may be written as a geometrical
sum
Components
of the acceleration
vector
Projections of the
acceleration
on the axis  and n
3
Thus, the derivative of the tangent unit vector with respect to the arc coordinate is perpendicular to the tangent of the path.
Thus, the total acceleration of the particle is the geometrical sum of two accelerations: tangential acceleration equal to the first derivative of the numerical value of the velocity, or the second derivative of the displacement with respect to time, and normal acceleration equal to the second power of the velocity divided by the radius of the curvature of the path at the given point of the path
The tangential acceleration is directed along the tangent to the path towards the arc coordinate increase if , (otherwise – in opposite sense).
The normal acceleration is directed towards the concavity of the path perpendicular to the tangent acceleration.
Module of the total acceleration

## Slide 45: Section 1 (continuation 1.4)
Uniformly Variable Curvilinear Motion. Curvilinear motion is called uniformly variable if the tangential acceleration is constant.
Let us write this equation in the form
As is constant integrating both members of the last equation over the corresponding intervals gives
Velocity of the particle is
By substituting the expression
for the velocity and by
Integrating we obtain
Velocity of the particle at
uniformly variable motion.
Law of uniformly
variable motion.
Special Cases of the Particle Motion
№ пп |  |  | Kind of motion | 
 |  |  | Velocity | Path
1 | = 0 [t, t1] | = 0 [t, t1] | uniform (v = const) | rectilinear ( = )
2 | = 0 [t, t1] |  0 [t, t1] | uniform (v = const) | curvilinear (  )
2.1 | = 0 at instant t | = 0 [t, t1] | nonuniform (v  const), at instant t v = max | rectilinear ( = )
2.2 |  |  0 [t, t1] |  | curvilinear (  )
3 |  0 [t, t1] | = 0 [t, t1] | nonuniform (v  const) | rectilinear ( = )
3.1 |  | = 0 at instant t | change in direction of motion (v = 0 at t=t) | any
3.2 |  |  | nonuniform (v  const) | fold of the path ( =  at t=t)
4 |  0 [t, t1] |  0 [t, t1] | nonuniform (v  const) | curvilinear (  )
5 | = const [t, t1] | any | uniformly variable | any
4

## Slide 46
Kinematics is a part of mechanics which treats of the geometrical aspects of the bodies' motion. By motion we mean any change in the relative positions of material bodies in space which occurs in the course of time.
To describe the motion, or the law of motion, of a given body means to specify the position of that body relative to a given frame of reference for any moment of time.
There are three methods of describing motion: the natural method, the coordinate method and the vector method.
The vector of instantaneous velocity of a particle is equal to the first derivative of the radius vector of the particle with respect to time.
The vector of instantaneous velocity is tangent to the path of the particle in the direction of motion.
The acceleration characterizes the time rate of change of the velocity in magnitude and direction.
The instantaneous acceleration of a particle is equal to the first derivative of the velocity vector or the second derivative of the radius
vector of the particle with respect to time.
The projections of the velocity on the coordinate axes are equal to the first derivatives of the corresponding coordinates of the particle with respect to time.
The projections of the acceleration on the coordinate axes are equal to the first derivatives of the projections of the velocities, or the second derivatives of the corresponding coordinates of the particle with respect to time.
The numerical value of the instantaneous velocity of a particle is equal to the first derivative of the displacement of the particle with respect to time.
The tangential acceleration characterizes the change of speed.
The normal acceleration characterizes the change of the velocity in direction.
Uniform rectilinear motion is the only case of motion in which the acceleration is continually zero.
The tangential acceleration of a particle is equal to the first derivative of the numerical value of the velocity, or the second derivative of the displacement with respect to time.
The normal (radial) acceleration is equal to the second power of the velocity divided by the radius of the curvature of the path at the given point of the curve.
5
Curvilinear motion is called uniformly variable if the tangential acceleration is constant.
Summary of Section 1

## Slide 47: Section 2
Kinematics of a Rigid Body. The principal problem is that of determining all the kinematic characteristics
of the motion of a body as a whole and of any of its particles.
There are following kinds of motion of a body:
1. Translational motion (slider, piston, plunger, compartment door, cabin of panoramic wheel).
2. Rotational motion (fly-wheel, crank, rocker, panoramic wheel, door).
3. Plane motion (connecting rod, locomotive wheel along rectilinear rails, abrasive disc).
4. Spherical motion (ball-and-socket, gyroscope).
5. Motion of a free rigid body (celestial body, aircraft).
Translation of a rigid body is such a motion in which any straight line through the body remains continually parallel to itself.
Translation should not be confused with rectilinear motion. In translation the particles of a body may move on any curved paths.
Theorem: In translatory motion, all the particle of a body move along similar paths and have at any instant the same velocity and acceleration.
C
A
B
A
B
Draw the vector AB joining two points.
It is obvious that at any instant the following equation is valid
The length of rBA is constant, being the distance between two points of a rigid body, and the direction
of rBA is constant by virtue of the translational motion of the body
It follows then that the path of the particle A can be obtained by a parallel displacement of all the points
of the path of the particle B through a constant vector rBA . Hence, the paths of particles A and B are
identical curves which will coincide if superimposed.
Differentiating both parts of the above equation with respect to time we obtain
i.e., at any instant the velocities of points A and B are equal in magnitude and direction
Differentiating again we obtain
i.e., at any instant the accelerations of points A and B are equal in magnitude and direction
Thus, the translational motion of a rigid body is fully described by the motion of any point belonging to it.
The analysis of translational motion of a rigid body is reduced to the methods of particle Kinematics.
6

## Slide 48: Section 2 (continuation 2.2)
Rotation of a rigid body is such a motion in which there is always two points of the body or two points continuously connected
with this body which remain motionless. The line through these fixed points is called the axis of rotation.
Description of the Rotational Motion. The position of the body at any instant will be fully specified by the angle  between the two planes, taken with the appropriate sign, which we shall call the angle of rotation of a body ( fixed plane P, passing through the axis of rotation, and a plane Q, rotating with a body).
P
Q
- equation of the rotational motion.
Angular Velocity is the time rate of change of the angle of rotation of a body.
the average angular velocity of the body in the time interval t.
Consider at t  0.
the angular velocity of the body at a given instant t.
If dφ/dt > 0, the rotation takes place towards the increase of the angle of rotation,
if dφ/dt < 0, the rotation takes place towards the decrease of the angle of rotation.
Angular Acceleration characterizes the time rate of change of the angular velocity of a body.
the average angular acceleration of the body in the time interval t.
Consider at t  0.
the angular acceleration of
the body at a given instant t.
If the angular velocity increases in magnitude, the rotation is accelerated, if it decreases, the rotation is retarded. It will be readily noticed that the rotation is accelerated when  and  are of the same sign, and retarded when they are of different sign.
Angular velocity is represented by the arc arrow towards the direction of rotation.
ω
Angular acceleration is represented by the arc arrow towards the increase of the angle of rotation if
ε
If the angular velocity of a rotating body does not change the rotation is said to be uniform.
If the angular acceleration of a body does not change during the rotation, the rotation is said to be uniformly variable.
7

## Slide 49: Section 2 (continuation 2.3)
Velocities of the Points of a Rotating Body
The path of the point is known. This is circumference of some radius R.
O
+
-
s
φ
R
The arc coordinate is
Then we obtain
Thus, the linear velocity of a point belonging to a rotating body is equal to the product of the angular velocity of that body by the distance of the point from the axes of rotation
The linear velocity is tangent to the circle described by point.
ω
As the value of  at any given instant is the same for all points of the body it follows that the linear velocity of any point
of a rotating body is proportional to its distance from the axis of rotation.
.
Accelerations of the Points of a Rotating Body
The path of the point is known. This is circumference of some radius R.
Then projections of the acceleration on the tangent to the circumference and on the normal are
Hence, the tangential acceleration is This acceleration, called rotary acceleration, is perpendicular to the radius.
ε
Normal acceleration, called centripetal, is directed along radius towards the axis of rotation. It equals
The accelerations of all the points of a rotating body are proportional to their distances from the axis
of rotation.
The total acceleration of a point is
The inclination of the vector of total acceleration to the radius
of the circle described by the point is specified by the angle
Vector Representation of the Angular Velocity and Angular Acceleration
The angular velocity of a body can be denoted by a vector along the axis of rotation in the direction from
which the rotation is seen counterclockwise.
ω
ε
ω
ε
z
z
By analogy with angular velocity, the angular acceleration of a body can be denoted by a vector along the axis of rotation. The direction of  coincides with that of  when the rotation is accelerated, and is of opposite sense when the rotation is retarded.
z, z – projections of the respective vectors on z-axis.
8

## Slide 50: Section 2 (continuation 2.4)
Vector Representation of the Velocity of a Point in Rotational Motion -
This formula defines both magnitude and direction of the velocity.
ω
Modulus of this vector product is
R
R
Hence,
The velocity vector is really has the same direction as the above mentioned cross-product, i.e., it is perpendicular to the plane through vectors and r in the direction from which a counterclockwise rotation would be seen to carry vector of angular velocity into radius-vector through the smaller angle.
The right-hand rule – at superposing of the thumb with the first vector and other fingers with the second vector, the turning
of the thumb perpendicular to the palm shows the direction of the cross-product.
.
Hence, the cross-product of the angular velocity of a body by the radius-vector of a particle determines completely the
modulus and direction of its velocity vector.
Vector Representation of the Rotational (Tangential) Acceleration of a Point in Rotational Motion -
This formula defines both magnitude and direction of the rotational acceleration.
The modulus of this cross-product is
Hence,
R
The direction of the rotational acceleration can be determined in accordance with the right-hand rule.
Hence, the cross-product of the angular acceleration of a body by the radius-vector of a particle determines the modulus and direction of its rotational acceleration.
ε
R
Vector Representation of the Centripetal (Normal) Acceleration of a Point in Rotational Motion -
This formula describes both magnitude and direction of the centripetal acceleration.
The modulus of this cross-product is
1, since the velocity vector is perpendicular to the vector of
the angular velocity.
ω
R
Hence,
Direction of the centripetal acceleration can be determined in accordance with the cross-product definition or the right-hand rule.
Hence, the cross-product of the angular velocity of a body by the velocity vector of a particle determines the modulus and direction of its centripetal acceleration.
This product may be represented as
9

## Slide 51: Section 2 (continuation 2.5)
Euler's Formulae – in accordance with the cross product definition one can obtain analytical expressions for the velocity of a point at arbitrary disposition of the rotational axis in space
ω
R
x
y
z
x
y
z
Whence we have analytical formulae for the velocity projections
Transformation of rotational motions – the change of the magnitude and direction of the angular velocities of the revolving members (links) in gears.
Frictional mesh
R1
R2
ω1
ω2
Velocities of the particles of the wheels at the point of contact in the absence of slippage are
Whence
Gear ratio characterizes the change of the angular velocity in rotational transmission from one gear to another. This is a ratio of the angular velocities of the driving and driven gears
Toothed Gear. The number of teeth is in direct proportion of the wheels radii. Velocities of the particles of the wheels at the point of contact, as before, are equal. The above equations are valid, including the case of the internal mesh.
R1
R2
ω1
ω2
The radii of the pitch circles are related with the teeth pitch
where and are the number of teeth. Then
Belt and chain transmission – velocities of the particles of the wheels at the point of contact with the belt or chain, as before, are equal ( the belts and chains are considered as inextensible).
The above equations remain valid
R1
R2
ω1
ω2
2
v
10

## Slide 52
Translation of a rigid body is such a motion in which any straight line through the body remains continually parallel to itself.
In translational motion, all the particles of a body move along similar paths and have at any instant the same velocity and acceleration.
The translational motion of a rigid body is fully described by the motion of any point belonging to it.
Rotation of a rigid body is such a motion in which there is always two points of the body or two points continuously connected with this body which remain motionless. The line through these fixed points is called the axis of rotation.
The angular velocity of a body at a given time is equal in magnitude to the first derivative of the angle of rotation with respect to time.
Angular acceleration characterizes the time rate of change of the angular velocity of a rotating body.
The angular acceleration of a body at a given time is equal in magnitude to the first derivative of the angular velocity, or the second derivative of the angular displacement, of the body with respect to time.
Both the angular velocity and the angular acceleration of a body can be represented by a vector along the axis of rotation.
The linear velocity of a point belonging to a rotating body is equal to the product of the angular velocity of that body and the distance of the point from the axes of rotation.
The linear velocity of a point belonging to a rotating body is equal to the product of the angular velocity of that body and the distance of the point from the axes of rotation.
The linear acceleration of a point belonging to a rotating body is equal to the geometrical sum of its tangential and normal acceleration.
If the angular velocity of a rotating body does not change the rotation is said to be uniform. If the angular acceleration of a body does not change the rotation is said to be uniformly variable.
11
The linear velocity and acceleration of any point of a rotating body are proportional to its distance from the axis of rotation.
Summary of Section 2

## Slide 53: Section 3
Plane Motion of a Rigid Body. Plane motion of a rigid body is such motion in which all its points move parallel to a fixed plane.
In investigating plane motion it is sufficient to investigate the motion of any section of a body parallel to a fixed plane.
All the points of the body belonging to a normal move in the same way.
M1
M2
Draw from fixed point O the radius-vectors and It is obvious that
O
In plane motion vector M1M2 doesn’t change its magnitude and direction, since we consider absolutely rigid body. Hence, the points of this vector describe identical paths and have at any instant the same velocity and acceleration.
Resolution of the Plane Motion into Translation and Rotation. Consider the successive positions
of some section of a moving body. It will be observed that the following method can be employed to move
this section. Let us first turn the section about the pole (point A) and then translate the body.
Thus, the plane motion of a rigid body is a combination of a translation, in which all the points move in the same way as the pole A, and of a rotation about that pole.
In analyzing a plane motion, we are free to choose any point of the body as a pole. The rotational component of motion does not depend on the position of the pole.
A
B
B1
A2
B2
A1
Equations of the Plane Motion of a Rigid Body. The position of any section is completely specified by the position of any line AB in this section. The position of the line AB may be specified by the coordinates xa and yA of point the A (pole) and the angle  between an arbitrary line AB and axis x. As the body moves, the quantities xa , yA and  will change with time, and the motion of the body at any moment of time will be completely described by equations
The translational component of the plane motion can, evidently, be described by the first two of these equations, and the rotational component by the third one. The principal kinematic characteristics of the plane motion are the velocity and acceleration of the translation, and the angular velocity and angular acceleration of the rotation about the pole.
A
B
x
xA
y
yA

xC
12

## Slide 54: Section 3 (continuation 3.2)
A
B
С
D
Independence of the Angular Velocity and Angular Acceleration on the Choice of the Pole. Take any two straight lines which depict position of a plane figure and two poles A and B.
The angles between these lines and horizontal axis are different and related by equation
A
B
B
A

By differentiating we obtain
Hence, the angular velocities of the lines are equal
Differentiating once again we conclude that accelerations are the same
Therefore, an angular velocity and angular acceleration of a body in plane motion do not depend on the pole choice, and they can be represented by the vectors perpendicular to the plane of motion.
z
Determination of the Velocity of a Point of a Body. Velocity of any point of a body is the geometrical sum of the velocity of any other point taken as the pole and the velocity of rotation of point about the pole.
.
The position of the point B is specified by the radius vector
Differentiating one can obtain
A
B
O
In this equation the first component is equal to the velocity of the pole A. The second is equal to the velocity of the point B at =const, i.e., when A is fixed or, in other words, when the section rotates about the pole A.
The velocity of rotation of the point B about pole A is . This velocity is perpendicular to AB.
x1
Corollary – The projections of the velocities of two points of a rigid body on the straight line joining those points are equal.
Projecting both members of the vector equation on x1 we obtain
It is obvious that for the points lying on the same straight line are valid the following equations:
A
B
C
b
c
13

## Slide 55: Section 4
Instantaneous Center of Zero Velocity (Instantaneous Center for Velocities). The instantaneous center of zero velocity is a point belonging to the section of a body or its extension which at the given instant is momentarily at rest.
Let the velocity of any point A and the angular velocity of a body be known.
A
According to the theorem of the composition of velocities, for the point P we have
Let the velocity of the point P be zero
Then one may obtain
This permits to determine the location of the instantaneous center of zero velocity. It is located on the perpendicular to the velocity of the point A, which is laid towards the angular velocity at a distance
A point of intersection of perpendiculars to the velocity vectors of any two points will be the instantaneous
center of zero velocity.
P
Thus, the velocity of the rotation of the point P about the pole A must be equal and parallel to the velocity of the point A and have opposite sense.
Taking a point P as the pole the velocities of any points A and B will be
Thus, the velocity of any point of a body is equal to the velocity of its rotation about the instantaneous center of zero velocity.
In other words, a plane motion is a result of consecutive infinitesimal rotations about instantaneous center of zero velocity
(instantaneous axis of rotation).
Therefore, the velocity of any point of a body is proportional to its distance from the instantaneous center of zero velocity.
These results lead to the following conclusions:
To determine the instantaneous center of zero velocity, it is sufficient to know the directions of the velocities of any two points A and B of a body
or their paths. The instantaneous center of zero velocity lies at the intersection of the perpendiculars erected from points A and B to their respective
velocities, or to the tangents to their paths.
2) The angular velocity of a body is equal to the ratio of the velocity of any point to its distance from the instantaneous center of zero velocity.
3) To determine the velocity of any point of a body, it is necessary to know the magnitude and direction of the velocity of any point A of that body and
the direction of the velocity of another point B of the same body.
B
P
C
14

## Slide 56: Section 4 (continuation 4.2)
Determination of the Velocity of a Point of a Body by Using the Instantaneous Center of Zero Velocity.
Consider some examples taking instantaneous center of zero velocity as a pole.
1
Given: vA, the location of the points A, B, C, there is no slippage.
Define: vB, vC .
B
C
A
If the plane motion is performed by a cylinder rolling without
slipping along a fixed surface, the point of contact P is
momentarily at rest and, consequently, is the
instantaneous center of zero velocity.
2) Find the angular velocity
P
3) Connect the points B and C with the instantaneous center and determine
velocities of these points
The arc arrow of the angular velocity is directed aside of vector vA.
Vectors vB and vC are directed aside of the arc arrow
of the angular velocity.
2
Given: vA, ω , the location of the points A, B, C.
Define: vB, vC.
The instantaneous center is on the perpendicular to
the vector vA.
2) Determine the distance to the
instantaneous center
3) Connect the points B and C with the instantaneous center and determine
velocities of these points
The distance AP put aside of the arc arrow of
the angular velocity.
Vectors vB and vC are directed aside of the arc arrow
of the angular velocity.
B
C
A
P
3
Given: vA, vB, the location of the points A, B, C.
Define: vC.
The instantaneous center is at the intersection of
perpendiculars to the vectors vA ,vB.
2) Find the angular velocity
The vector vC is directed aside of the arc arrow
of the angular velocity.
B
C
A
P
The arc arrow of the angular velocity is directed aside of
vectors vA , vB.
3) Connect the point C with the instantaneous center and
determine the velocity of this point
4
Given: vA, the path of the point B, the location of the points A, B, C.
Define: vC.
1) The instantaneous center is at the intersection of
perpendiculars to the vector vA and tangent to the path of
the point B.
2) Find the angular velocity
The vector vC is directed aside of the arc arrow
of the angular velocity.
The arc arrow of the angular velocity is directed aside of
vectors vA , vB.
Connect the point C with the instantaneous center and
determine the velocity of this point
B
C
A
P
15

## Slide 57: Section 4 (continuation 4.3)
5
Given: vA, vB, vA║vB, the location of the points A, B, C.
Define: vC.
1) The Instantaneous center is on the perpendicular to
the vector vA and vB. This point lies in infinity.
2) This state of motion is called instantaneous translation.
The angular velocity of the body
at the given instant is zero.
3) The velocities of all points of the body are equal in magnitude
and direction at every instant
6
Given: vA, vB, vA║vB, the location of the points A, B, C.
Define: vC.
The instantaneous center is on the perpendicular to the vector vA and vB. These perpendiculars merge into one line.
2) Define the location of
the instantaneous center
and the angular velocity
3) Connect the point C with the instantaneous center
and determine the velocity of this point
The arc arrow of the angular velocity is directed
aside of the vector vA and vB.
B
C
A
B
C
A
P
7
Given: vA, vB, vA║vB, the location of the points A, B, C.
Define: vC.
1) The instantaneous center is on the
perpendicular to the vector vA and vB. These
perpendiculars merge
into one line.
2) Define the location of
the instantaneous center
and the angular velocity
3) Connect the point C with the instantaneous center and
determine the velocity of this point
The arc arrow of the angular velocity is directed
aside of the vector vA and,vB.
The vector vC is directed aside of the arc arrow of the angular velocity.
B
C
A
P
Determination of the Acceleration of a Point of a Body.
The acceleration of any point of a body is composed of the acceleration of any other point taken for the pole and the acceleration of the point in its rotation together with the body around that pole.
It was shown that for any two points is valid the following equation:
Differentiate it with respect to time
Differentiate the second component
as a product of two functions
Therefore,
A
B
C
a
b
16

## Slide 58
The plane motion of a rigid body is such a motion in which all its points move parallel to a fixed plane.
The plane motion of a rigid body is a combination of a translation, in which all the points move in the same way as a pole, and of a rotation about that pole.
The velocity of any point of a body is the geometrical sum of the velocity of any other point taken as a pole and the velocity of rotation of a point around that pole.
The projections of the velocities of two points of a rigid body on the straight line joining those points are equal.
The instantaneous center of zero velocity is a point belonging to the section of a body or its extension which at the given instant is equal to zero.
The velocity of any point of a body is equal to the velocity of its rotation about the instantaneous center of zero velocity.
The acceleration of any point of a body is composed of the acceleration of any other point taken for the pole and the acceleration of the point in its rotation together with the body around that pole.
The angular velocity of a body at any given instant is equal to the ratio of the velocity of any point to its distance from the instantaneous center of zero velocity.
17
Summary of Section 4

## Slide 59: Section 5
Resultant Motion of a Particle. Relative, Transport, and Absolute Motion
In solving problems of mechanics it is often more expedient (and sometimes necessary) to consider the motion of a particle or body simultaneously with respect to two frames of reference, one of which is assumed to be fixed and the other moving in some specified way with reference to the first. The motion performed in this case is called resultant, absolute or combined motion.
For example, when a sphere rolls on the deck of a moving boat, its motion with respect to the shore is the resultant of its rolling relative to the deck (the moving frame of reference) and its motion together with the deck with respect to the shore (the fixed frame of reference).
Consider the resultant motion of a particle M moving with respect to a frame of reference Oxyz, connected with some moving body, which is in turn moving
with relation to another frame of reference O1,, which we assume to be fixed. We employ the following definitions:
z



O1
x
y
M
x
y
z
O
The motion performed by the particle M with respect to the moving coordinate system is called relative motion (r).
The motion performed by the moving frame of reference Oxyz, together with all the points of space fixed with respect
to it, relative to the fixed system O1, is for the particle M, the motion of transport (e).
The motion of the particle with respect to the fixed frame of reference is called the absolute, or resultant, motion (a).
The path described in absolute motion is called the absolute path, the velocity, is the absolute velocity (va ),
and the acceleration, the absolute acceleration ( aa ).
The path described by the particle in relative motion is called the relative path. The velocity of the motion of the
particle relative to the axes Oxyz is called the relative velocity (vr), and the particles acceleration in that motion
is the relative acceleration (ar).
The velocity of the point fixed in the moving axes Oxyz with which the particle M coincides at a given instant is called
the transport velocity of the particle M at that instant (ve), and the acceleration of that point is called
the transport acceleration of the particle M (ae).
Composition of Velocities. Theorem: in resultant motion the absolute velocity of a point is the geometrical sum of the relative velocity
and the transport velocity. At any instant it is valid the following relation:
Differentiate this relation with respect to time taking into account that unit vectors i, j, k change their direction
The first component is the velocity vO; the next three – relative velocity of the point (vr).
Define derivatives of the unit vectors i, j, k
taking into account the formula from the
section 2.

ωe
Substitute the cross products into the last three components
The sum of the first and the last component is the velocity of the free body's point, i.e. transport velocity (ve)
Thus, taking into account that the derivative of the radius-vector 
is the absolute velocity we obtain
The magnitude of the
absolute velocity is
18

## Slide 60: Section 5 (continuation 5.2)
■ Composition of Accelerations. Coriolis Theorem: the absolute acceleration of a particle is equal to the geometrical sum of the
relative acceleration, the transport acceleration, and the Coriolis acceleration.
For the velocity we have obtained
Differentiate this relation with respect to time
The first component is the acceleration aO; the next three – relative acceleration of the point ar .
Define the derivatives of the unit vectors i, j, k
Substitute these relations into the last three components.
The sum of the first and the obtained last components represents the acceleration of the free body's point, i.e. transport acceleration ae
By transforming and rearranging we obtain
This component of acceleration is called
Coriolis acceleration (ac)
Thus, taking into account that the second derivative of the radius-vector  is the absolute acceleration we obtain
■ Determination of Coriolis Acceleration.
Modulus of Coriolis acceleration is
Coriolis acceleration is zero when
1)  = 0, if the motion of transport is translational or if the angular velocity
of the rotation of transport becomes zero at a given instant;
2) if there is no relative motion or if the relative velocity becomes zero at
a given instant;
if the relative motion is parallel to the axis of the rotation of transport.
Direction of Coriolis acceleration.
The direction of Coriolis acceleration can be
obtained by
1) projecting vector of the relative velocity
on the plane, which is normal to the vector of
the angular velocity,
2) turning that projection through 900 in
the direction of the rotation of transport.
19

## Slide 61: Section 5 (continuation 5.3)
■ Origination of Coriolis Acceleration.
Consider the example. Assume that the magnitude of the relative linear velocity of a point and the angular velocity of a body is constant.
ωe
ωe
In some time interval the point will move away from the axis of rotation and the body will turn through some angle.
As a result:
The relative velocity changes in direction because of the transport motion and
The transport linear velocity changes because of the relative motion (the distance between the axis of rotation and a point changes).
Hence, there are two causes of Coriolis acceleration origination:
1) The transport motion affects on the relative velocity, and
2) The relative motion, in turn, has an influence on the transport velocity.
Therefore, the absolute acceleration of a particle is equal to the geometrical sum of three accelerations: the relative acceleration, which characterizes the time rate of change of the relative velocity in the relative motion, the transport acceleration, which characterizes the time rate of change of the transport velocity in the transport motion, and the Coriolis acceleration, which characterizes the time rate of change of the relative velocity in the transport motion and of the transport velocity in the relative motion.
■ Determination of Coriolis Acceleration (Examples).
Consider the motion of a point on the Earth's surface.
20

## Slide 62
The motion performed by a particle with respect to the moving coordinate system is called relative motion. The path described by the particle in relative motion is called the relative path. The velocity of the motion of a particle relative to the moving axes is called the relative velocity, and the particles acceleration in that motion is the relative acceleration.
The motion performed by the moving frame of reference, together with all the points of space fixed with respect to it, relative to the fixed system is for a particle, the motion of transport.
The velocity of the point fixed in the moving axes with which a particle coincides at a given instant is called the transport velocity of the particle, and the acceleration of that point is called the transport acceleration of the particle.
The motion of the particle with respect to the fixed frame of reference is called the absolute, or resultant, motion. The path described in this motion is called the absolute path, the velocity, is the absolute velocity, and the acceleration, the absolute acceleration.
In resultant motion the absolute velocity of a point is the geometrical sum of the relative velocity and the transport velocity.
The absolute acceleration of a particle is equal to the geometrical sum of three accelerations: the relative acceleration, which characterizes the time rate of change of the relative velocity in the relative motion, the transport acceleration, which characterizes the time rate of change of the transport velocity in the transport motion, and the Coriolis acceleration, which characterizes the time rate of change of the relative velocity in the transport motion and of the transport velocity in the relative motion.
The Coriolis acceleration is zero when:
1) The motion of transport is translational or if the angular velocity of the rotation of transport becomes zero at a given instant;
2) There is no relative motion or if the relative velocity becomes zero at a given instant;
3) The relative motion is parallel to the axis of rotation.
The Coriolis acceleration of a particle is equal to the double vector product of the angular velocity of the motion of transport and the relative velocity of the particle.
21
Summary of Section 5

## Slide 63: Section 6
■ Resultant Motion of a Rigid Body. If a body moves with respect to a set of moving axes which are in transport motion
relative to a fixed system, the resulting motion of a body is called absolute or combined motion. The problem in this case is to determine the
relation between the parameters of the relative, transport, and absolute motion.
■ Composition of Translational Motions. In translational motion all the points have the same velocity. From the theorem of the composition of particle's
velocities we have
Thus, the absolute motion of two translational motions is also a translational motion with a velocity equal to the geometrical sum of the
translational and transport velocity of a body.
■ Composition of Rotations About two Parallel Axes. The disc rotates about its axis passing trough the point O1, with the angular velocity r, and this axis, in turn, rotates about a fixed axis passing trough the point O, with the angular velocity e.
O
O1
An arbitrary point A of the disk makes combined motion (moves in a circular path in the moving plane, rigidly connected to the crank OO1). The absolute velocity of
this point is
A
The problem of determining the velocity of any of the points of the disc can be simplified if we find the position of the instantaneous center of rotation K.
Whence
It means that this point lies on the segment OO1
and divides it into parts, inversely proportional to the angular velocities. Hence,
K
To determine the absolute angular velocity consider the point O1, which is not involved in the relative motion, and define its velocity twice (in translational motion and absolute motion). These velocities should be the same
Represent the segment OO1, as the sum OO1 =O1K+OK, then
Whence
In the case of the opposite direction of rotations it can be shown that the division of the segment OO1 is inversely proportional to the angular velocities, but only externally (the point K lies on the same line out of the segment OO1 from the greater angular velocity). Then OO1 =O1K-OK and the absolute angular velocity is
Both relations can be combined with one vector equation
Thus, the absolute angular velocity is the geometric sum of the relative and transport angular velocities.
There is a complete analogy between the vector composition of angular velocities and the composition of two parallel forces.
The sum of the forces is their resultant applied at a point dividing the distance between the forces at the segments, inversely proportional to the forces.
22

## Slide 64: Section 6 (continuation 6.2)
■ Couple of Rotations. It is known that the couple of forces has not a resultant. A couple is characterized by its moment.
By analogy, two parallel equal in magnitude and oppositely directed angular velocities, called a couple of rotations, has a zero resultant angular velocity. The result represents a translational motion, the velocity of which is determined by the moment of rotation couple.
d
Thus, the resultant motion will be a translation with a velocity equal
to the moment of rotation couple.
Similarly, the reverse procedure is also possible - a representation of
translational motion as a rotation couple.
■ Composition of Rotations About Two Intersecting Axes. Consider a body rotating with an angular velocity r about its own axis passing through the point of intersection O with the other axis of rotation. The second axis rotates with an angular velocity e.
O
The velocity vector of the translational motion of a rigid body is a free vector (can be moved parallel to itself) while the angular velocity vectors are sliding
vectors, which can only move along the line of action.
Since the point of intersection of the axes of rotation has a zero speed, then taking it for a fixed point
in space, we can calculate the velocity of a point M by the theorem of the composition of velocities
M
The vector sum of the angular velocities obtained in parentheses represents the resulting angular
velocity determined by a single rotation of the body about an instantaneous axis (spherical
motion), which can be regarded as an absolute angular velocity
Thus, the absolute angular velocity is equal to the geometric sum of the relative and transport
angular velocity
When adding more than two rotational motions the resulting angular velocity is equal to
the geometric sum of all angular velocities involved in a combined motion
23

## Slide 65: Section 6 (continuation 6.3)
■ Composition of Rotation and Translation. Let the body be in the rotational motion with the angular velocity ω and translational motion with the velocity v. The angle  between the angular velocity and translational velocity is arbitrary.
Decompose the vector of the translational velocity on the two mutually perpendicular vectors such that one coincides with the
angular velocity
O
The velocity vector v1 is represented as a couple of rotations
with the angular velocities equal to a given angular velocity of the
rotational motion
A
Transport the vector of the translational velocity v*, as a free vector, to the point A. Two vectors of the angular velocities, shown at the point O, can be removed, since they are equal in magnitude and oppositely directed
The distance OA is defined from the equality of the velocity and the moment of the couple of rotations
Thus, we have obtained a rotation with the angular velocity ω about an axis passing through the point A, and the translational motion with the velocity v*. Such a combination can not be simplified. It represents a kinematic screw (a screw motion of a rigid body). The axis passing through the point A along the angular velocity is called an instantaneous screw axis.
■ Velocity of the Point of a Body in a Screw Motion. Let the body be involved in the rotational motion with an angular velocity ω1,
which we take for the relative motion, and translational motion with the speed v*, which is taken for the transport motion
A
M
The absolute velocity of the point M is
The point M moves along a helical path making one revolution in time T
During the time T the point M moves in the direction of the translational velocity by the value h (screw pitch)
The ratio of the translational velocity and the angular velocity is a characteristic of the screw motion. It called a screw parameter
Then the screw pitch is
The module of the absolute velocity of the point M is
In the particular case when  =900 ( the translational velocity is perpendicular to the angular velocity) the motion is reduced
to a single rotational motion about an axis passing through the point A
24

## Slide 66
The absolute motion of two translational motions is also a translational motion with a velocity equal to the geometrical sum of the translational and transport velocity of a body.
The absolute angular velocity is the geometric sum of the relative and transport angular velocities.
Two parallel equal in magnitude and oppositely directed angular velocities are called a couple of rotations.
A couple of rotations has a zero resultant angular velocity. The result represents a translational motion, the velocity of which is determined by the moment of rotation couple.
The size of the translational displacement of any point lying on the axis of the screw during one complete turn is called the path of the screw.
If the resultant motion of a body consists of a rotation and a translation, which velocity is parallel to the angular velocity, it is called a screw motion. The axis which passes trough the vector of the angular velocity is called the axis of the screw.
25
The pitch of the screw is .
Summary of Section 6

## Slide 67: THEORETICAL MECHANICS
Part III Dynamics

## Slide 68: Contents
Content of the part III corresponds to the educational and vocational program on Electric power engineering, Electrotechnics and Electromechanics, particularly, to the subject of Theoretical Mechanics. Notions of Dynamics are considered. Examples of practical problem solutions are represented.
Section 1. Basic Concepts and Definitions. The Laws of Dynamics. The Problems of Dynamics for a Free and a Constrained Particle. Solution of the First Problem of Dynamics.
Section 2. Differential Equations of Motion for a Particle and Their Integration. Rectilinear Motion of a Particle. Curvilinear Motion of a Particle. Solution of Problems. Motion of a Particle Thrown at an Angle to the Horizon in a Uniform Gravitational Field.
Section 3. Vibration of a Particle. Free Harmonic Motion. Damped Vibration.
Section 4. Damped Forced Vibrations. Resonance.
Section 5. Dynamics of a System. Mechanical Systems. External and Internal Forces. Mass of a System. Centre of Mass. Momentum of a Particle and a System. Impulse of a Force. Theorem of the Motion of the Center of Mass. The Law of Conservation of Motion of the Center of Mass. Theorem of the Change in the Momentum of a Particle. Theorem of the Change in Linear Momentum of the System. The Law of Conservation of the Linear Momentum.
Section 6. Angular Momentum of a System. Theorem of the Change in the Angular Momentum of a Particle. Theorem of the Change in the Total Angular Momentum of a System. The Law of Conservation of the Total Angular Momentum. Moment of Inertia of a Body About an Axis. Radius of Gyration. Moments of Inertia of a Body About Parallel Axes. Moments of Inertia of Some Homogeneous Bodies. Differential Equation of Rotational Motion of a Body. Solution of Problems.
Section 7. Work Done by a Force. Power. Kinetic Energy of a Particle and a System. Examples of Calculation of Work. Theorem of the Change in the Kinetic Energy of a Particle and a System. Solution of Problems.
Section 8. Use of the Theorem of the Change in the Kinetic Energy of a System. Potential Force Field. Force Function. Potential Energy of a System. Dynamics of Translational and Rotational Motion of a Rigid Body. Compound Pendulum.
Section 9. Dynamics of a Plane Motion of a Rigid Body. D’Alembert’s Principle for a Particle and a System. The Principal Vector and the Principal Moment of the Inertia Forces of a Rigid Body. Examples.
Section 10. Analytical Mechanics. Generalized Coordinates. Equations of Constraints. Ideal Constraints. Virtual Displacements of a System. Degrees of Freedom. The Principle of Virtual Work. Solution of Problems.
Section 11. The General Equation of Dynamics. Solution of Problems. Generalized Forces.
Section 12 . Lagrange’s Equations. Kinetic Potential. Conditions of Equilibrium in Terms of Generalized Coordinates. Solution of Problems.
REFERENCES
1. Бондаренко А.Н. «Курс лекций по теоретической механике. Динамика», Москва – 2007, www.miit.ru/institut/ipss/faculties/trm/main.htm
2. S. Targ. Theoretical Mechanics. A Short Course. Moscow: Foreign Languages Publishing House, 421 p.
3. I.V. Meschersky. Collection of Problems in Theoretical Mechanics. – Moscow: The Higher School Publishing House, - 304 p.
4. A. Pytel, J. Kiusalaas. Engineering Mechanics: Dynamics, Third Edition, Cengage Learning ,200 ,First Stamford Place, Suite 400, Stamford, CT 06902, USA, - 673 p.
ii

## Slide 69: Section 1
Dynamics is that section of mechanics which treats of the laws of motion of material bodies subjected to the action of forces.
Unlike kinematics, in dynamics the motion of bodies is investigated in connection with the acting forces and the inertia of the material bodies themselves.
Dynamics of a Particle
Dynamics
Dynamics of a System
Analytical Mechanics
■ A particle is a material body (a body possessing mass) the size of which can be neglected in investigating its motion.
The inertia of a body depends on the amount of matter it contains.
The quantitative measure of the inertia of body, which depends on the quantity of matter in the body, is called the mass of that body.
Fundamental assumptions:
– There exists absolute space (it is independent on matter and its motion).
– There exists absolute time (it is independent on matter and its motion).
From here follows:
– There exists absolutely fixed frame of reference.
– Time is independent on the motion of reference.
– Mass is independent on the motion of reference.
■ The Laws of Dynamics. The study of dynamics is based on laws generalizing the results of a wide range of experiments and observations of the motions of bodies, i.e., laws that have been verified in the long course of human history.
■ The First Law (the Inertia Law): a particle free from any external influences continues in its state of rest, or of uniform rectilinear motion, except in so far as it is compelled to change that state by impressed forces.
The inertia law states one of the basic properties of matter: that of being always in motion. It establishes the equivalence, for material bodies, of the states of rest and of motion under no forces. A frame of reference for which the inertia law is valid is called an inertial system (or, conventionally, a fixed system).
■ The Second Law (the Fundamental Law of Dynamics). It states: the product of the mass of a particle and the acceleration imparted to it by a force is proportional to the acting force; the acceleration takes place in the direction of the force
The mass of a body is equal to its weight divided by the acceleration of gravity
In S.I. of units, the unit of a force is called newton (briefly written as N). It may be defined as the force while acting upon a mass of one kg produces an acceleration of 1 in the direction of which it acts.
■ A mechanical system is defined as such a collection of material points (particles) or bodies in which the position or motion of each particle or
body of the system depends on the position and motion of all the other particles or bodies. We shall thus regard a material body as a system
of its particles.
1

## Slide 70: Section 1 (continuation – 1.2)
Differential equations of the particle motion
- Vector form of the differential equation.
- Coordinate form of differential
equations.
These equations is a result of projecting vector equation (1).
By grouping we obtain three
scalar equations
Coordinate form. Use the relation between radius-vector, coordinates of a particle and projections of a force
or
Substitute acceleration of a particle into basic equation of Dynamics
M(x,y,z)
O
Natural form. Project vector equation (1) on natural (moving) coordinate axes
- Natural form of differential
equations.
M
O
M
■ The basic equation of Dynamics
■ Superposition of forces. The acceleration of material point under the action of a few forces is equal to the geometrical sum of accelerations
of a point from the action of each of forces separately. or
It should be noted that the forces of interaction between free particles (or bodies) do not form a balanced system, as they act on different objects.
■ The Third Law (the Law of Action and Reaction) establishes the character of mechanical interaction between material bodies. It states: two particles
exert on each other forces equal in magnitude and acting in opposite directions along the straight line connecting the two particles.
m1
m2
2

## Slide 71: Section 1 (continuation – 1.3)
The Problems of Dynamics for a Free and a Constrained Particle
The problems of dynamics for a free particle are: 1) knowing the equation of motion of a particle, determine the force acting on it (the first problem of dynamics); 2) knowing the forces acting on a particle, determine its equation of motion (the second, or principal, problem of dynamics).
In engineering it is often necessary to investigate constrained motions of a particle, i.e., the cases when constraints attached to a particle compel it to move along a given fixed surface or curve. In such cases we shall use, as in statics, the axiom of constraints.
For the constrained motion the first problem of dynamics will usually be: determine the reactions of the constraints acting on a particle if the motion and applied forces are known. The second (principal) problem of dynamics for such motion will pose two questions: knowing the applied forces, to determine: a) the equation of motion of the particle and b) the reaction of its constraints.
Solution of the First Problem of Dynamics
Example 1. A lift of the weight P starts ascending with acceleration. Determine the tension in the cable.
1. We choose an object (a cage is in translational motion and it can be examined as a particle).
2. Discard the constraint (cable) and replace it by the reaction R.
3. Write the basic equation of Dynamics
Define the reaction of the cable
Define the rope tension
At the uniform motion of the cage ay = 0 and the tension of the cable equals the weight T = G.
At break of the cable T = 0, and its acceleration is equal to the acceleration of a free falling ay = -g.
3
4. Project this equation on y-axis
y
Example 2. A particle of the mass m moves in horizontal plane Oxy according to equations x = acoskt, y = bsinkt. Determine the force acting on a point.
y
x
x
y
1. We choose an object (the particle).
2. Discard the constraint (plane) and replace it by the reaction N.
3. Add unknown force F.
4. Write the basic equation of Dynamics
5. Project this equation on x and y-axis
Determine the projections of a force
The modulus
of a force is
The direction of a force can be determined from the formulas
Thus, the magnitude of a force is proportional to the distance of a particle to the center of coordinates and
directed to the center on a line, connecting a particle with a center.
A path of motion of the particle is an ellipse with the center at the beginning of coordinates
O
r

## Slide 72: Section 1 (continuation – 1.4)
Examle 3. A weight G is suspended by a thread of the length l from a fixed point 0. It represents a conical pendulum as it traces a circular path on a horizontal plane. The thread forms an angle with the vertical. Determine the velocity of the weight and the tension T in the thread.
1. We choose an object (weight).
2. Discard the constraint (cable) and replace it by reaction R.
3. Write the basic equation of dynamics:
From the third equation we determine
reaction of the cable
Determine the tension of the cable
Substitute the reaction of the cable and normal acceleration into the second equation, determine the velocity of the weight
4. Project this equation on axes ,n, b
Example 4. An automobile weighing G runs over an arched bridge with the speed v. The radius of the curvature of the bridge at its mid-point is R. Determine the pressure which the automobile exerts on the bridge at the instant when it passes over the center of the bridge.
1. We choose an object (automobile, it can be examined as a particle).
R
2. Discard the constraint (rough surface) and replace it by reaction N and force of friction Ffr.
3. Write the basic equation of dynamics
4. Project this equation on the axis n
whence determine the normal reaction:
Determine the pressure on the bridge
Whence one can define the velocity which corresponds to zero pressure on a bridge (Q = 0)
4

## Slide 73
Dynamics is that section of mechanics which treats of the laws of motion of material bodies subjected to the action of forces.
Inertia is the property of material bodies to resist a change in their velocity under the action of applied forces.
The quantitative measure of the inertia of body, which depends on the quantity of matter in the body, is called the mass of that body.
The First Law (the Inertia Law): a particle free from any external influences continues in its state of rest, or of uniform rectilinear motion, except in so far as it is compelled to change that state by impressed forces.
The Second Law (the Fundamental Law of Dynamics): the product of the mass of a particle and the acceleration imparted to it by a force is proportional to the acting force; the acceleration takes place in the direction of the force.
The Third Law (the Law of Action and Reaction): For two particles it states: two particles exert on each other forces equal in magnitude and acting in opposite directions along the straight line connecting the two particles.
For constrained motion the first problem of dynamics is: to determine the reactions of the constraints acting on a particle if the motion and applied forces are known.
The second (principal) problem of dynamics for constrained motion: knowing the applied forces, to determine: a) the equation of motion of the particle and b) the reaction of its constraints.
The problems of dynamics for a free particle are: 1) knowing the equation of motion of a particle, to determine the force acting on it (the first problem of dynamics); 2) knowing the forces acting on a particle, to determine its equation of motion (the second, or principal, problem of dynamics).
5
Summary of Section 1

## Slide 74: Section 2
From the initial conditions we can determine the constants C1 …C6
and develop finally the equation of motion for the particle in the form
Thus, under the action of the same force system a particle can make a
class of motions which is determined by the initial conditions. The initial
coordinates determine the starting point position. The initial velocity,
given by their projections, takes into account the initial kinematic state of the particle.
Differential Equations of Motion for a Particle and Their Integration. The forces acting on a particle can depend on time, on the position of the particle and its velocity. Projecting the basic equation of dynamics on coordinate axes we have three equations of the second order
After integrating we have six arbitrary constants
C1, C2,…., C6.
The constants C1, C2,…., C6 are determined from initial conditions at t = 0
Example 1. (Force is constant). A free particle of the mass m moves under the action of a force F, constant in magnitude and direction. At the initial time the point had a speed v0 which coincides with the direction of a force. Determine the law of motion.
1. Write the basic equation of dynamics
3. Deflate the derivative
2. Choose the frame of reference by directing the x-axis along the direction of a force and project
the equation on this axis or
x
y
z
4. Separate variables
5. Define integrals in both parts of equation
6. Represent the projection of the velocity as a
derivative of the coordinate with respect to time
8. Define integrals in both parts of equation
7. Separate variables
9. Determine the integration constants C1 … C6 , assuming for the specific problem the initial conditions
at t = 0, vx = v0 , x = x0.
As a result, we have obtained the equation of uniformly variable motion along x-axis
6

## Slide 75: Section 2 (continuation – 2.2)
Example 2. (Force depends on time). A body of the weight P starts moving from rest along a smooth horizontal plane under the action of a force F the magnitude of which increases in proportion to the time, the relation being F = kt. Develop the equation of motion for the body.
3. Write the basic equation of dynamics
5. Deflate the derivative
4. Project equation on x-axis or
7
6. Separate the variables
7. Calculate the integrals in both sides of the equation
9. Represent the projection of the velocity as a
derivative of the coordinate with respect to time
11. Calculate the integrals in both sides of the equation
10. Separate the variables
8. Determine the constant of integration from the initial condition t = 0, vx = v0=0
As a result we obtain
x
y
x
O
1. Take the frame of reference (Cartesian coordinates), so that the body had a positive coordinate.
2. Consider the body as a material point (the body is in a translational motion), relieve it from constraint and replace it
by the normal reaction of a smooth surface.
12. Determine the constant C2 from initial condition t = 0, x = x0=0
Example 3. (Force depends on coordinate). A material point of the mass m is thrown upward from the Earth with the speed v0. The force of Earth's gravity is inversely proportional to the square of the distance from the point to the center of gravity (the center of the Earth). Determine the dependence of the speed on the distance y to the center of the Earth.
1. Take the frame of reference (Cartesian coordinates), so that the body had a positive coordinate.
x
y
y
O
2. Write the basic equation of dynamics
3. Project this equation on y-axis or
The coefficient of proportionality can be found using the weight of a point on the Earths surface
R
Hence the differential equation is or
4. Deflate the derivative
5. Replace the variable
6. Separate the variables
7. Integrate both sides of the equation
8. Substitute the limits
Finally, we obtain the expression
for the speed as a function of the coordinate y
The maximum height of flight
can be found equating the
velocity to zero
The maximum altitude when the denominator tends to zero. Whence
Hence, when substituting the radius of the Earth and acceleration of a free fall it turns out the second space speed

## Slide 76: Section 2 (continuation – 2.3)
Example 4. (Force depends on velocity). A boat of the mass m is pushed and receives an initial velocity Assuming the resistance of the water at low velocities to be proportional to the first power of the velocity and changing according to the equation, determine the time in which the velocity will drop by one-half and the distance the boat will travel in that time. Determine also the distance the boat will travel till it stops.
8
1. Let us choose the origin O to coincide with the initial position of the boat, pointing the axis Ox in the direction of the motion.
x
y
x
O
2. Consider the boat as a material point (it is in a translational motion), relieve it from constraint (water) and replace it
by reaction (buoyancy force) and a force of resistance of the water.
3. Add an active force ( the weight of the boat).
4. Write the basic equation of dynamics
5. Project this equation on x-axis or
6. Deflate the derivative
7. Separate variables
8. Calculate the integrals
in both sides of the equation
9. Substitute the limits
Whence we can determine time of motion
The required time is determined by assuming .
To determine the distance, it is better to write the differential equation of motion in other form, replacing variables. We thus obtain
Integrating and substituting the limits we have
The distance travelled by the boat till it stops
■ Motion of a Particle Thrown at an Angle to the Horizon in a Uniform Gravitational Field
x
y
x
O
Eliminating the time t in the last equation, we obtain the equation of the path
Equating y to zero we determine the
time of flight
The horizontal range can be defined by substituting the time of flight

## Slide 77
General Pointing to the Solution of Problems
The method of integrating the differential equations of motion includes the following operations:
1. Write the differential equation of motion.
1.1. Choose an origin (usually coinciding with the initial position of the particle) and draw a coordinate axis along the line of motion, as a rule in the direction of motion; if, for the applied forces a particle has a position of equilibrium, it is convenient to choose the origin coinciding with the position of the static equilibrium.
9
1.2. Draw the moving particle in an arbitrary position and depict all the forces acting on the particle.
1.3. Add up the projections of all the forces on the coordinate axis and substitute the sum into the right side of the differential equation of motion.
It is important to express all the variable forces in terms of the quantities on which they depend.
2. Integrate the differential equation of motion.
The integration is carried out according to the rules of higher mathematics, depending on the form of the obtained equation, i.e., on the form of the right-hand member of the equation.
2.1. Separate the variables, for example or
2.3. Calculate indefinite integrals in both sides of the equation
2.2. If there are three variables in the equation of
motion, make the change of variables, for example and then separate variables.
2.4. Determine the constants of integration. In order to determine the constants of integration it is necessary to define the initial conditions from the
statement of the problem, for example at t = 0, vx = vx0, whence
3. Express a speed through the derivative of the coordinate with respect to time and repeat the items 2.1, 2.3 and 2.4.
4. Determine the required quantities and analyze the obtained results. In order to be able to analyze the solution and also to verify the
dimensions the solution should be carried out in the most general form (in the letter notation), inserting the numerical data only in the final results.
These general rules also hold good for curvilinear motion.
Summary of Section 2

## Slide 78: Section 3
Vibrations of a Particle
There exists a restoring force R directed towards a fixed center O and proportional to the distance from that center. This force tends to return a point in a state of equilibrium .
10
There exists a restoring
force; the state of equilibrium is stable.
A restoring force is absent;
the state of equilibrium
is unstable.
A restoring force is absent;
the state of equilibrium
is indifferent.
There exists a restoring force;
the state of equilibrium
is stable.
x
y
O
Kinds of Vibrations
1. Free Harmonic Motion.
2. Damped Vibration.
3. Undamped Forced Vibrations.
4. Damped Forced vibrations.
■ Free Harmonic Motion
Consider a particle moving rectilinearly under the action of a restoring force R directed towards a fixed center O and proportional to the distance from that center. Write the basic law of dynamics
Take a coordinate system with the origin at the point O and project this equation on x-axis
Writing the differential equation of motion, we obtain
This equation is the differential equation of a free harmonic motion.
Referring to the theory of differential equations we have
Since the roots of a characteristic equation are imaginary,
its general solution will be
The velocity of the point is
Initial conditions
Determine the constants of integration
A restoring force R is

## Slide 79: Section 3 (continuation – 3.2)
11
Therefore, the equation of a free harmonic motion is
If we replace and by constants a and , such that and we obtain
where a – amplitude,  - initial phase.
Define a and 
x0=asin
T
- period of harmonic vibration
a – amplitude of vibration

## Slide 80: Section 3 (continuation – 3.3)
12
Damped Vibration
Let a moving particle be acted upon by a restoring force R and a resisting force F.
Let us see how the resistance of a surrounding medium affects vibrations, assuming the resisting force proportional
to the first power of the velocity
 - viscosity factor.
x
y
O
The basic equation of dynamics is
By projecting on x-axis we obtain
Dividing both sides by m, we get
where
The characteristic equation has the roots
The general solution depends on the kinds of the roots.
1. n < k – the case of the small viscous resistance. - the roots are complex and different.
or
x = ae-nt
x = -ae-nt
The frequency of damped vibrations is
The period is
T*
Damping decrement -
ai
ai+1
Logarithmic decrement -
It follows that a small resistance has practically no effect on the period of vibration, but gradually damps it by virtue of the amplitude of vibration decreasing according to a law of geometric progression.
2. n > k – the case of the great viscous resistance. - the roots are real and different.
or
- this function is aperiodic.
x
t
x
t
3. n = k. - the roots are real, multiple.
this function is aperiodic.

## Slide 81: Section 3 (continuation – 3.4)
x
y
O
с1
с2
Classification of Solutions of the Differential Equations
Differential equation | Characteristic equation | Roots of the characteristic equation |  | Solution of the differential equation | Graph
 |  | n<k |  |  | 
 |  | n>k |  |  | 
 |  | n=k |  |  | 
x
t
x
t
Spring Connection. Equivalent Stiffness
y
y
x
O
с1
с2
x
O
с1
с2
13

## Slide 82: Section 4
Forced Vibrations
Consider the motion of a particle on which are acting a restoring force R and a disturbing force .
Disturbing force may be of different nature. For example, it may be as a result of the inertial effect of the unbalanced mass m1 in a rotor.
x
y
O
x
y
O
A


The basic equation of dynamics is
By projecting on x-axis we obtain
Reduce this equation to
the standard form
14
This equation is the differential equation of forced vibration of a particle. Its general solution, as is known, has the form x=x1+x2, where x1 is the
general solution of the equation without the right side, , and x2 is a particular solution of the complete equation.
Let us find the solution x2 in the following form:
The last equation must be satisfied at any instant t.
Therefore or
Thus, the obtained vibrations are compounded of natural vibration (the first term in the final solution, x1) and forced vibration (the second term in the final solution, x2).
If p < k (the forced vibrations have a small frequency),
the phase of vibrations coincides with the phase of a disturbing
force
As a result we obtain or
The general solution is
The constants С1 and С2, or a and  have to be determined from initial conditions using the complete equation.
Hence, the particular solution is
If p k (the forced vibrations have a great frequency),
the phase of vibrations is opposite to the phase of a disturbing
force

## Slide 83: Section 4 (continuation – 4.2)
15
Dynamic Factor is a ratio of the amplitude of forced vibrations and static elongation of a point under the action of the constant force H = const
The amplitude of forced vibrations is
The static elongation may be determined from the equilibrium equation
where
whence
Thus, at p < k (small frequency of
forced vibrations) the dynamic
factor is
At p > k (great frequency of
forced vibrations) dynamic
factor is
0
1
2
3
3
2
1
If p = k (the frequency of forced vibrations equals frequency of natural vibrations) the amplitude of forced vibrations becomes very large. This phenomenon is called resonance.
Lack of the balance in working machines and motors, for example, usually causes resonance to appear in the machine or its foundation.
The differential equation in this case is
The general solution is
Substitute into differential equation
Take the particular solution in a form and calculate the derivatives
Hence, we have the following solution or
Thus, with no damping force the vibration amplification process in resonance conditions is unlimited and the amplitude increases indefinitely.
Damped Forced Vibrations.
The differential equation of damped forced vibration of a particle is
The general solution depends on the ratio of n and к (see section 3, slide 12).
Let us find the particular solution in the form and determine derivatives
Substituting into differential equation we obtain
For this equation to be satisfied at any instant of time, the factors of the same trigonometric functions in the left and right sides should be separately equal. Hence,
Squaring and adding these equations we obtain
Dividing one equation by the other, we obtain the phase shift of forced vibrations
Hence, the law of damped forced vibrations at n < k (small resistance) is
1) The amplitude of forced vibrations does not depend on the initial conditions.
2) Forced vibration does not die out in the presence of resistance.
3) The frequency of forced vibration is equal to the frequency of the disturbing force and does not depend on the characteristics of the vibrating system.
4) Even when the disturbing force is small, large forced vibration can be induced if the resistance is small and the frequency p is almost equal to k (resonance).
5) Even if the disturbing force is large, forced vibrations can be damped if the frequency p is much larger than k.

## Slide 84
The differential equation of free harmonic motion is where
The law of a free harmonic motion is
Properties of a free harmonic motion: 1) The amplitude and initial phase depend on the initial conditions; 2) The frequency k, and the period T, do not depend on the initial conditions; 3) A constant force does not change harmonic motion, but only shifts the center of vibrations in the direction of the action of the force by the static elongation.
The differential equation of damped vibration where
The law of damped vibration where .The period
The differential equation of damped forced vibration of a particle is
The law of a damped vibration , where .
A small resistance has practically no effect on the period of vibration, but gradually damps it by virtue of the amplitude of vibration decreasing according to a law of geometric progression.
16
Properties of a forced vibration:
1) The amplitude of forced vibration does not depend on the initial conditions.
2) Forced vibration does not die out in the presence of resistance.
3) The frequency of forced vibration is equal to the frequency of the disturbing force and does not depend on the characteristics of the vibrating system (the disturbing force "impresses" its own vibration frequency on the system).
4) Even when the disturbing force is small, large forced vibration can be induced if the resistance is small and the frequency p is almost equal to k (resonance).
5) Even if the disturbing force is large, forced vibration can be damped if the frequency p is much larger than k.
Summary of Sections 3- 4

## Slide 85: Section 5
Dynamics of a System
A mechanical system is defined as such a collection of material points (particles) or bodies in which the position or motion of each particle or body of the system depends on the position and motion of all the other particles or bodies. We shall thus regard a material body as a system of its particles.
A collection of bodies not connected by interacting forces does not comprise a mechanical system.
17
External and Internal Forces. External forces are defined as the forces exerted on the members of a system by particles or bodies not belonging
to the given system. Internal forces are defined as the forces of interaction between the members of the same system.
We shall denote external forces by the symbol , and internal forces by the symbol. Both external and internal forces can be either active forces or
the reactions of constraints.
The division of forces into external and internal is purely relative, and it depends on the extent of the system whose motion is being investigated.
In considering the motion of the solar system as a whole, for example, the gravitational attraction of the sun acting on the earth is an internal force;
in investigating the earth's motion about the sun, the same force is external.
S
E
M
Internal forces possess the following properties:
The geometrical sum (the principal vector) of all the internal forces of a system is zero.
This follows from the third law of dynamics, which states that any two particles of a system act on each other with equal and oppositely directed forces, the sum of which is zero. Since the same is true for any pair of particles of a system, then
2. The sum of the moments (the principal moment) of all the internal forces of a system with respect to any
center or axis is zero.
These equations can be rewritten in other form
It does not follow from the above that the internal forces are mutually balanced and do not affect the motion of the system, for they are applied to different particles or bodies and may cause their mutual displacement. The internal forces will be balanced only when a given system is a rigid body.
Mass of a System. Centre of Mass. The mass of a system is equal to the arithmetical sum of the masses of all the particles or bodies comprising it
The center of mass or center of inertia, of a system is defined as a geometrical point C whose coordinates are given by the equation
or
The concepts of center of gravity and center of mass, however, are not identical. The concept of center of gravity, as the point through which the resultant of the forces of gravity passes, has a meaning only for a rigid body in a uniform field of gravity.

## Slide 86: Section 5 (continuation – 5.2)
18
Theorem of the Motion of Center of Mass
Consider a system of n particles. Write the differential equations of motion for every particle of a system and add them
or
Bring under the differential sign
For the radius vector of the center of mass we have
Substitute into obtained equation
or
Projecting both sides of the
last equation on the coordinate
axes, we obtain
The center of mass of a system moves as if it were a particle of mass equal
to the mass of the whole system to which are applied all the external forces
acting on the system.
The Law of Conservation of Motion of Center of Mass
Let the sum of the external forces acting on a system be zero
It follows, then, that or
Thus, if the sum of all the external forces acting on a system is zero, the center of mass of that system moves with a velocity of constant magnitude and direction, i.e., uniformly and rectilinearly. In particular, if the center of mass was initially at rest it will remain at rest. The action of the internal forces, we see, does not affect the motion of the center of mass.
Example: Two men of the masses m1 and m2 are seated in the boat of the mass m3. Neglecting the resistance of the water, determine the displacement of the boat if the man of the mass m2 went at a distance а to the bow.
а
2. Let the sum of the projections of external forces acting on a system on one of
the coordinate axes be zero Then
Thus, if the sum of the projections on an axis of all the external forces acting on a
system is zero, the projection of the velocity of the center of mass of the system on
that axis is a constant quantity. In particular, if at the initial moment it will
remain zero at any subsequent instant, i.e., the center of mass of the system will not
move along the x-axis
1. Choose an object (a boat with men).
2. Discard the constraint (water) and replace it by reaction (buoyancy force).
3. Add active forces.
5. Write the theorem of the motion of the center of mass
Project on x-axis
x
y
O
Define how far it is necessary to change the seat of the man of the mass , so that the boat was at the initial position
The boat moves at a distance l in the opposite direction.

## Slide 87: Section 5 (continuation – 5.3)
Impulse of a Force
The concept of impulse (or linear impulse) of a force is used to characterize the effect on a body of a force acting during a certain interval of time
19
Projections of impulse on coordinate axis are
When the force is constant, we get
Then its projections are
Impulse of a resultant is equal to the geometrical sum of the impulses of all the forces applied to the particle during the same time interval
Multiply by dt
Take definite integral in a given time interval
Momentum of a Particle. The momentum of a particle is defined as a vector quantity equal to the product of the mass of the particle and its velocity
m
Theorem of the Change in the Linear Momentum of a System
Consider a system of n particles. Writing the differential equations of motion for this system, we obtain or
Linear Momentum of a System. The linear momentum, or simply the momentum, of a system is defined as the vector quantity equal to the geometric sum (the principal vector) of the momenta of all the particles of the system
For the radius vector of the center
of mass we have
The momentum of a system is equal to the product of the mass
of the whole system and the velocity of its center of mass.
Then
Projections of the momentum of a system are
The derivative of the linear momentum of a system with respect to time is equal to the geometrical sum of all the external forces acting
on the system.
Add these equations
Bring under the differential sign
From the definition of the momentum of a system
In terms of projections on Cartesian axes we get

## Slide 88: Section 5 (continuation – 5.4)
Euler's Theorem - Application of the Theorem of the Change in the Linear Momentum of a System to the Motion of Continuous Medium (water)
1. We choose as an object of motion the volume of water, being in the curvilinear channel of turbine.
2. Discard constraints and replace them by reactions (Rs - resultant of superficial forces).
3. Add active forces (Rv - resultant of volume forces).
4. Write the theorem of the change in the linear momentum of a system
The linear momentum of water at instants t0 and t1 can be presented as sums
A
B
C
A
B
C
D
D
The change in the linear momentum of water in time interval [t0,t1] is
The change of the linear momentum of water for an infinitesimal time dt is
, where
F1
F2
Taking the product of density, cross sectional area and a speed for the second mass we get
Substituting this differential into theorem we obtain
Let the momentum of a system be at time , and at time t1 let
it be . Multiplying both sides of preceding equation by dt and integrating, we obtain
or .
This equation states the theorem of the change in the linear momentum of a system in integral form: the change in the linear momentum of a system during any time interval is equal to the sum of the impulses of the external forces acting on the system during the same interval of time.
In terms of projections on Cartesian axes we have
, ,
The Law of Conservation of the Linear Momentum
Let the sum of all the external forces acting on a system be zero
It follows, then, that in this case
Thus, if the sum of all the external forces acting on a system is zero, the momentum vector of the system is constant in magnitude and direction.
Let the external forces acting on a system be such that the sum of their
projections on any axis Ox is zero It follows that in this
case
Thus, if the sum of the projections on any axis of all the external
forces acting on a system is zero, the projection of the momentum of
that system on that axis is a constant quantity.
Hence, the geometrical difference of the second linear momenta of liquid equals the sum of the principal vectors of the volume and superficial forces.
20
In projections on axes

## Slide 89
A mechanical system is a collection of material points (particles) or bodies in which the position or motion of each particle or body of the system depends on the position and motion of all the other particles or bodies.
External forces are defined as the forces exerted on the members of a system by particles or bodies not belonging to the given system. Internal forces are defined as the forces of interaction between the members of the same system.
The geometrical sum (the principal vector) of all the internal forces of a system is zero.
The sum of the moments (the principal moment) of all the internal forces of a system with respect to any center or axis is zero.
The mass of a system is equal to the arithmetical sum of the masses of all the particles or bodies comprising it.
The center of mass or center of inertia, of a system is defined as a geometrical point C whose coordinates are given by the equations
The linear momentum of a system is defined as the vector quantity equal to the principal vector of the moments of all the particles of the system.
The momentum of a system is equal to the product of the mass of the whole system and the velocity of its center of mass.
The momentum of a particle is defined as a vector quantity mv equal to the product of the mass of the particle and its velocity.
21
Elementary impulse is defined as a vector quantity equal to the product of the vector of a force and the time element dt.
Summary of Section 5
The impulse of a force in any time interval t1 is equal to the integral of the elementary impulse over the interval from zero to t1.

## Slide 90
The center of mass of a system moves as if it were a particle of mass equal to the mass of the whole system to which are applied all the external forces acting on the system.
If the sum of all the external forces acting on a system is zero, the center of mass of that system moves with a velocity of constant magnitude and direction, i.e., uniformly and rectilinearly.
If the sum of the projections on an axis of all the external forces acting on a system is zero, the projection of the velocity of the center of mass of the system on that axis is a constant quantity.
The change in the momentum of a particle during any time interval is equal to the geometric sum of the impulses of all the forces acting on the particle during that interval of time.
The change in the linear momentum of a system during any time interval is equal to the sum of the impulses of the external forces acting on the system during the same interval of time.
If the sum of the projections on any axis of all the external forces acting on a system is zero, the projection of the momentum of that system on that axis is a constant quantity.
If the sum of all the external forces acting on a system is zero, the momentum vector of the system is constant in magnitude and direction.
22
Summary of Section 5
The geometrical difference of the second linear momenta of liquid equals the sum of the principal vectors of the volume and superficial forces.

## Slide 91: Section 6
23
Theorem of the Change in the Angular Momentum
The moment of the vector with respect to any center or axis is called the moment of momentum or angular momentum with respect to that center or axis
Total Angular Momentum of a System
The total angular momentum of a system with respect to any center 0 is defined as the quantity , equal to the geometrical sum of the angular momenta of all the particles of the system with respect to that center
m
r
O
In the terms of projections
on the axes
By projecting we get
Write the basic equation of dynamics for each particle of a system or
Sum up these equations
for all particles
But the sum of derivatives equals the derivative of the sum
The expression in brackets is the angular momentum of a system. Hence,
Consider the following cross product:
We can take the sign of the derivative
beyond the cross product
Hence, we obtain
The derivative of the total angular momentum of a system about any fixed center with respect to time is equal to the sum of the moments of all the external forces acting on that system about that center.
By projecting both sides of the last equation on a set of fixed axes Oxyz, we get
The derivative of the total angular momentum of a system about any axis with respect to time is equal to the sum of the moments of all the external forces acting on that system about that axis.

## Slide 92: Section 6 (continuation – 6.2)
24
■ The Law of Conservation of the Total Angular Momentum
1. If the sum of the moments of all external forces acting on a system taken with respect to any center is zero (Moe = 0), the total angular momentum of the system with respect to that center is constant in magnitude and direction KO = const.
2. If the sum of the moments of all the external forces acting on a system with respect to any axis is zero Mxe = 0, the total angular momentum of the system with respect to that axis is constant Kx = const.
Similar statements hold for the axes y and z.
■ Moment of Inertia of a Body is
m
O
h
h
The moment of inertia of a particle with respect to a given axis Oz is defined as a product of its mass multiplied by the square of its perpendicular distance from the axis.
mk
O
hk
The moment of inertia of a body with respect to a given axis Oz is defined as a scalar quantity equal to the sum of the masses of the particles of the body, each multiplied by the square of its perpendicular distance from the axis.
■ Moment of Inertia of a Body about an Axis.
Moment of Inertia of a particle is
If we divide a body into elements, in the limit
the sum will become an integral and we obtain
moment of inertia about an axis.
Moment of inertia is a
measure of a body's inertia in
rotational motion.
product of inertia.
polar moment of inertia.
■ The Parallel-Axis (Huygens') Theorem
The moment of inertia of a body with respect to any axis is equal to the moment of inertia of the body with respect to a parallel axis through the center of mass of the body plus the product of the mass of the body by the square of the distance between the two axes.
dm
O1
O2
Moment of inertia about initial axis
Statics moments about initial axes
Body's mass
Distance between the
axes z1 and z2
Hence,
If axis z1 passes through the center of mass,
then the static moments are zero.

## Slide 93: Section 6 (continuation – 6.3)
25
■ Thin Homogeneous Rod of the Length L and Mass M
x
z
L
Consider an elementary volume
dV = Adx at the distance x.
x
dx
An elementary mass is
To calculate the moment of inertia about the central
axis (passing through the center of gravity) it is sufficient to change
axis location and specify the limits of integration (-L / 2, L / 2).
Use the parallel-axis theorem.
zС
■ Circular Homogeneous Cylinder or Disc of the Radius R and Mass M
H
R
dr
r
Consider an elementary volume
dV = 2πrdrH (thin cylinder of the radius r)
An elementary mass is
Here we used the formula for the volume of the cylinder V = πH.
To calculate the moment of inertia of a hollow (thick) cylinder
it suffices define the limits of integration from R1 to R2 (R2> R1)
■ Thin Cylinder (Shell, t <<R )
H
R
t
C
In view of the smallness of the thickness of the cylinder believe that all points are
at the same distance from the axis R
and integration is not required.
The volume is V = 2πRtH (a thin cylinder
of radius R with wall thickness t). Then
The same can be obtained using the formula for a thick-walled cylinder, given the smallness of t
Since the height of the cylinder is not included in the formulas of moments of inertia, they remain true for a thin solid disc and rim (thin ring).
■ Angular Momentum of a Rotating Body with Respect to its Axis of Rotation.
Select a discrete small volume of the mass mi
Or passing to infinitesimal
The angular momentum of a rotating body with respect to the axis of rotation is equal to the product of the body's moment of inertia by its angular velocity.
■ Moments of Inertia of Some Homogeneous Bodies

## Slide 94: Section 6 (continuation – 6.4)
26
■ Differential Equation of Rotation of a Rigid Body About an Axis
Write the theorem of change in angular momentum
of a rigid body rotating around a fixed axis
The angular momentum of a rotating rigid body is
The sum of the moments of external forces relative to
the axis of rotation equals torque (reaction and gravity
force do not create the moments)
Substitute the angular momentum and torque in the theorem
Example: A man of the weight holds one side of the rope while another man of the equal weight is attached to the other end of
the rope. What would happen if the man starts climbing up the rope with the velocity u relative to the rope? The weight of the pulley is
one quarter that of the man's weight . Assume that the mass of the pulley is distributed uniformly along its rim.
1. Select the object of motion (pulley with men).
2. Discard constraints (support).
3. Replace the constraints by reactions (bearing).
4. Add the active forces (gravity).
5. Write a theorem of the change in the angular momentum of a system about the axis of rotation of the pulley
R
Since the sum of the moments of the external forces vanishes, the angular momentum must remain constant
At the initial instant the system was in equilibrium, so Kz0 = 0.
After the start of the motion of the man with respect to the rope the whole system was set in motion, but the angular momentum of the system must remain equal to zero 0, Kz = 0. The angular momentum of the system is made up of angular momentum of both men and the pulley
Here v2 is a speed of the second man, which is equal to the speed of the cable,
Example: Determine the period of free oscillations of a small homogeneous mass M and the rod of the length l, suspended by one end to a fixed axis of rotation.
x
y
z
С
O
Or
In the case of small oscillations sinφ φ.
The oscillation period is
The moment of inertia of the rod is

## Slide 95
The angular momentum is a moment of the linear momentum with respect to a center or an axis.
The derivative of the angular momentum of a particle about any axis (center) with respect to time is equal to the moment of the acting force about the same axis (center).
The total angular momentum of a system with respect to any axis (center) is defined as the quantity, equal to the geometrical sum of the angular momenta of all the particles of the system with respect to that axis (center).
The derivative of the total angular momentum of a system about any fixed center with respect to time is equal to the sum of the moments of all the external forces acting on that system about that center.
If the sum of the moments of all external forces acting on a system taken with respect to any center (axis) is zero, the total angular momentum of the system with respect to that center (axis) is constant.
The radius of gyration is equal to the distance from the axis to a point, such that if the mass of the whole body were concentrated in it the moment of inertia of the point would be equal to the moment of inertia of the whole body.
The moment of inertia of a body with respect to any axis is equal to the moment of inertia of the body with respect to a parallel axis through the center of mass of the body plus the product of the mass of the body by the square of the distance between the two axes.
The moment of inertia (mass moment) of a body with respect to a given axis is defined as a scalar quantity equal to the sum of the masses of the particles of the body, each multiplied by the square of its perpendicular distance from the axis. The mass moment is a measure of a body's inertia in rotational motion.
27
The angular momentum of a rotating body with respect to the axis of rotation is equal to the product of the moment of inertia of the body and its angular velocity.
Summary of Section 6
The differential equation of rotation of a rigid body about the axis is .

## Slide 96: Section 7
Work Done by a Force. Power
The concept of the work is introduced as a measure of the action of a force on a particle (body) in a given displacement, specifically that action which is represented by the change in the magnitude of the velocity of a moving particle.
Author | Measure of mechanical motion | Measure of mechanical interaction
Descartes | Linear momentum | Impulse of a force
Leibniz | Kinetic energy | Work of a force
First let us introduce the concept of elementary work done by a force in infinitesimal displacement ds. The elementary work done by a
force is defined as a scalar quantity This definition corresponds to the concept of work as a characteristic of that action of a force which tends to change the magnitude of velocity.
M
If angle is acute, the work is of positive sign. In particular, at , the elementary work
If angle is obtuse, the work is of negative sign. In particular, at , the elementary work
If angle , i.e., if a force is directed perpendicular to the displacement, the elementary work done by the force is zero.
The elementary work can be defined as a scalar quantity
An analytical expression for elementary work is
The work done by a force in any finite displacement MM1 is calculated as the integral sum of the corresponding
elementary works
or or or
Particular cases: 1. A force is constant in magnitude (F = const)
and direction ( =const)
2. A force is constant in magnitude (F = const)
and parallel to the displacement ( =0)
3. A force is directed perpendicular to the displacement
28
Power. The term power is defined as the work done by a force in a unit of time (the time rate of doing work). If work is done at a constant
rate, the power is where is the time in which the work is done. In the general case

## Slide 97: Section 7 (continuation – 7.2)
It is possible to prove the following statements:
■ The work of the resultant on some displacement is equal to the algebraic sum of works of the component forces on the same displacement.
■ The work of a constant force in compound motion is equal to the algebraic sum of works of this force on each of the motion.
■ The work done by all the internal forces of a non-deformable body is zero.
■ The work done by gravity does not depend on the path along which the point of its application moves. Forces possessing this property are called conservative forces.
The work done by a force applied to a rotating body. The elemental work done by the force applied to the body is
ω
R
d
ds


h
h – arm of a force about an axis.
z
The work of a force applied to
the rotating body is expressed
through the moment of a force
relatively this axis.
For the constant moment we have
■ The work done in a rotation through a finite angle.
The power in this case is
■ The work done by friction is where s is the length of the path.
■ The work done by frictional forces acting on a rolling body is where is the displacement of the center of the wheel, N - normal reaction, k– coefficient of rolling friction, R- radius of the wheel.
■ The work done by an elastic force (reaction of a spring).
29

## Slide 98: Section 7 (continuation – 7.3)
Kinetic Energy of a Particle and a System
■ The kinetic energy of a
particle is a scalar quantity equal
The kinetic energy of a system is defined as a scalar quantity equal to the
arithmetical sum of the kinetic energies of all the particles of the system
■ Translational motion.
■ Rotational motion.
■ Plane motion.
Theorem of the Change in the Kinetic Energy of a Particle
The change in the kinetic energy of a particle in any displacement is equal to the algebraic sum of the work done by all the forces acting on the particle in the same displacement.
Consider the equation , which expresses the fundamental law of dynamics.
Express the acceleration through the speed and
multiply left and right hand side of the equation by
the differential of radius vector
Integrating both sides of this equation in the limits
between the corresponding values of the variables at
points and M, we obtain
Theorem of the Change in the Kinetic Energy of a System
The change in the kinetic energy of a system during any displacement is equal to the sum of the work done by all the external and internal forces acting on the system in that displacement.
The theorem just proved is valid for any particle of a system
If we make up similar equations for all the particles of a system and add them up, we obtain
where T and denote the kinetic energy of the system at the beginning and the end of the displacement.
For non-deformable systems we get
30

## Slide 99: Section 7 (continuation – 7.4)
Example: A projectile of the mass m is thrown by the spring from the channel at an angle  to the horizon. The nonstretched length of a spring of the stiffness c is equal to the channel length l0. Before firing spring is compressed by an amount d. Determine the velocity of the projectile on leaving the channel, as well as the maximum flight altitude.
Given: , c, d, m, l0.
Define: v1, H.

d
1. Choose an object - a projectile.
2. Reject constraints – a barrel and a spring.
3. Replace the constraints by reactions - N, R.
4. Add an applied force – G.
5. Write a theorem of the change in the kinetic energy of a particle
Initial speed of the projectile is zero
The work of the forces applied to the object equals
The work of the normal reaction is zero (its direction is perpendicular to the displacement )
The work of the force of gravity is
The work of the elastic force of the spring (coincides with the direction of the motion ) is
Substitute defined values into the theorem
whence the speed of the projectile flight is
Define the maximum flight altitude
(repeat steps 1-5)
H
The vertical velocity of the projectile at the highest point of the path is zero
The horizontal velocity of the projectile is constant (the law of conservation of the particle momentum) and equal to
The work of gravity is
Substitute defined values into the theorem
After some transformations we have
Hence, the maximum
altitude is
Note that the preceding expression can be more quickly obtained by writing the theorem of the change in kinetic energy only for the vertical velocity of the particle, because there are no horizontal forces and horizontal velocity does not change .
31

## Slide 100
The elementary work done by a force is as a scalar quantity equal to the product of the projection of the force on the tangent to the path in the direction of the displacement by an infinitesimal displacement of the particle along that tangent.
The work done by a force in any finite displacement is calculated as the integral sum of the corresponding elementary works.
The work done by a gravitational force
The work done by an elastic force
The work done by friction
The work done by frictional forces acting on a rolling body
The power is defined as the work done by a force in a unit of time (the time rate of doing work).
The kinetic energy of a particle is a scalar quantity equal. The kinetic energy of a system is defined as a scalar quantity equal to the sum of the kinetic energies of all the particles of the system. Translational motion
Rotational motion: Plane motion:
The work done in a rotation through a finite angle
32
The change in the kinetic energy of a particle in any displacement is equal to the algebraic sum of the work done by all the forces acting on the particle in the same displacement.
Summary of Section 7
The change in the kinetic energy of a system during any displacement is equal to the sum of the work done by all the external and internal forces acting on the system in that displacement.
The work done by all the internal forces of a non-deformable system is zero.

## Slide 101: Section 8
Example: The massive paper roll of the radius R, set in motion by a push, rolls without slipping on inertia up rough inclined plane at an angle  to the horizon with a certain initial velocity. Coefficient of rolling friction is frol. Determine the necessary initial speed in order that it could cross the top of the height H from the starting position.
Given: , frol , H, R.
Define: v0.

1. Choose an object – roll.
2. Reject constraints – inclined plane.
3. Replace the constraints by reactions – N, Ffr, Mrol.
4. Add an applied force - G.
5. Write a theorem of the change in the kinetic energy of a system
Kinetic energy on the top is zero
The work of the forces applied to the roll equals
The work of the normal reaction is zero
The work of gravity is
The work done by the moment resisting rolling is
Substitute defined values into the theorem
Note that the expression for the initial speed does not depend on the mass of the roll.
Kinetic energy at initial instant is
Mass moment of inertia of the solid
roll is
Angular velocity is
Hence, the kinetic energy at initial instant equals
The work of the frictional force is zero (it is applied at the instantaneous center
The moment resisting rolling is
The difference of the turning angles is
After some transformations we get
Potential Field of Force
A force field is defined as a region of space in any point of which a particle experiences a force of certain magnitude and direction.
If the forces of the field depend only on coordinates F = F(x, y, z), the force field is said to be conservative (gravitational field, the field of elastic forces).
If the forces of the field depend also on time or velocity F = F(x, y, z, t, v), the force field is said to be non-conservative or dissipative
(electromagnetic field).
33

## Slide 102
■ Potential force field - a field in which there exists a function satisfying at every point the following relations:
where U = U(x, y, z) is a force function.
Section 8 (continuation – 8.2)
The force function is determined up to a constant
The main properties of the force function
1. Elementary work of a force of the potential field is the total differential of the force function
■ 2. The total work of a force of the potential field does not depend on the path of the point and is equal to the difference of values of the force function in the initial and final positions
Corollary: The work of a force of the potential field on displacement of the particle along a closed path is zero
x
y
z
The potential energy of the system is a function characterizing the amount of the energy (potential energy) at this point of the potential force field. The potential energy is equal to the work of the forces of the potential force field acting on the particle, at its motion from a given position to the initial (zero).
For a system of particles the potential energy is the sum of the work of the forces of the potential field on all displacements of the particles to the initial position.
The magnitude of the potential energy in the initial position is set to be zero П(x0,y0,z0) = 0.
At any point the potential energy is a function of coordinates П(x,y,z).
– relation between the potential energy and the force function.
Taking into account that П(x0,y0,z0) = 0 the last relation can be written as a difference
Since the potential energy is defined up to a constant, the work of a force of potential field on displacement from a point M0 to a point M is
Thus, the change of the potential energy is inverse in the sign and equal to the change of the force function. Hence,
34

## Slide 103: Section 8 (continuation – 8.3)
Examples of potential force fields
Field of gravity. Gravity, whose work does not depend on the path, is an example of the force, which has the potential - the locus of points in space where the potential energy is constant. The projections of the force of gravity on the coordinate axis are
The last expression is the differential equation that can be easily solved by separation of variables and integration of the left and right sides
x
y
z
x
y
z
Equipotential surfaces (П = const) are horizontal planes. The force of gravity is perpendicular to these planes in the direction of decreasing values of the potential energy.
The work of the gravity in displacement from a point M1 to point M2 is
■ Field of the central gravity. The force of gravity can be considered parallel and constant in magnitude only in a small area of space in the Earth's gravitational field and equipotential surfaces can be considered flat only within this area. When considering the force of attraction to the Earth's center the value of a force is directly proportional to the mass and inversely proportional to the square of the distance between the particle and the center of gravity O.
x
y
z
x
y
z
The projections of the attractive force are
The elementary work of the attractive force is
The differential of the potential
energy equals
This expression is a differential equation, which can be easily solved by integrating the left and right sides
Equipotential surfaces (П = const) of the central gravitational field are spherical surfaces with the center at point O. The attractive force is directed along the normal to these surfaces in the direction of decreasing values of the potential energy.
O
The Law of Conservation of Mechanical Energy
In the motion of a system subjected to the action of only conservative forces, the sum of the kinetic and potential energies of the system remains constant.
From the theorem of the change in kinetic energy of a system we have
whence
The sum of the potential and kinetic energy is called the total energy of the system.
35

## Slide 104: Section 8 (continuation – 8.4)
Dynamics of Translational and Rotational motion of a Rigid Body
Considered theorems for dynamics of a system provide differential equations describing the two types of motion of a rigid body.
Differential equations of translational motion of a rigid body follow from the theorem of the motion of the center of mass
Differential equations of rotational motion of a rigid body about a fixed axis follow from the theorem of the change in the angular momentum of a system
Any rigid body free to oscillate about a fixed horizontal axis under the action of gravity is called a compound, or physical, pendulum. In the event of a pendulum deviation from its equilibrium position occurs restoring moment of gravity, the existence of which is a condition of the oscillating motion (swing) with respect to the equilibrium position.
x
y
z
С
O
1. Select the object (the pendulum).
2. Reject constraints (hinge).
3. Replace the constraints by reactions (reaction of a hinge).
4. Write the differential equation of rotational motion about the x-axis
Represent the equation in the form - differential equation of oscillations of a physical pendulum.
Consider the mathematical pendulum of the length l
x
y
z
O1
O
Substitute the moment of inertia
and represent the equation in the form - differential equation of oscillations of a simple pendulum.
Since these equations differ only in the coefficients, it is possible to consider a physical pendulum as a mathematical pendulum with period of oscillation equal to the period of the physical pendulum. For this equate the coefficients
Whence we can define the reduced length of the physical pendulum
The last inequality is
easy to prove
The point of the physical pendulum at a distance l in a straight line OC is called the center of oscillation of the pendulum.
O1
In the case of small oscillations sinφ  φ. Then
Period of oscillation is
Using the formula for the period of oscillation we can determine empirically the moments of inertia of bodies of a complex shape (the center of gravity can be found by hanging).
36

## Slide 105
A field of a force is defined as a region of space in any point of which a particle experiences a force of certain magnitude and direction.
If the forces of the field depend only on coordinates, the force field is said to be conservative.
If the forces of the field depend on time or velocity, the force field is said to be non-conservative or dissipative.
The potential force field is a the field in which there exists a function satisfying at every point the relations , Y, .
Elementary work of a force of the potential field is the total differential of the force function.
The total work of a force of the potential field does not depend on the path of the point and is equal to the difference of values
of the force function in the initial and final positions.
The potential energy of a system is a function characterizing the amount of the energy (potential energy) at this point of the potential force field. The potential energy is equal to the work of the forces of the potential force field acting on the particle at its motion from a given position to the initial (zero).
For a system of the particles the potential energy is the sum of the work of the forces of the potential field in all displacements of the particles to the initial position.
The work of a force of the potential field in displacement of the particle along a closed path is zero.
37
The Law of Conservation of Mechanical Energy
In the motion of a system subjected to the action of only conservative forces, the sum of the kinetic and potential energies of the system remains constant.
Summary of Section 8
Differential equations of translational motion of a rigid body =, =, =.
Differential equation of rotational motion of a rigid body about a fixed axis .

## Slide 106
Dynamics of the Plane Motion of a Rigid Body
Plane motion can be represented as a combination of the translational motion of the body at a velocity of the center of mass and rotational motion around the center of mass. This representation has been used previously in the calculation of the kinetic energy
The first two differential equations describing the translational motion of the body,
we find, using the theorem of the motion of the center of mass
Differential equations of the plane motion of a rigid body. In the kinematics equations of a plane motion were obtained
when used as a pole any arbitrary point. In the dynamics the center of the mass is chosen as a pole.
The third differential equation describing the rotational motion around the center of mass of the body, we find, using the theorem of the change in angular momentum of a system
Likewise, using general theorems of dynamics the corresponding equations can be obtained for other more complex types of a rigid body motion (spherical, free, impact interaction).
D'Alembert's Principle (Hermann, Euler) is a common method by which the dynamic equations have the form of the equations of statics. Due to the simplicity this method has been widely used in many engineering disciplines.
D'Alembert's Principle for a Particle. The main equation of dynamics is
Transfer the product of the mass by acceleration in the right-hand side
The force, equal in magnitude to the product of the mass of the particle and its acceleration and directed oppositely to the acceleration, is called the inertia force of the particle
Thus, if at any given moment to the active forces and the reactions of the constraints acting on a particle is added the inertia force, the resultant force system will be in equilibrium and all the equations of statics will apply to it
.
Example 1. A lift of the weight P starts ascending with acceleration. Determine the tension in the cable.
1. Select the object ( the cabin of the lift).
2. Reject the constraint (cable) and replace it by reaction R.
3. Add the force of inertia
4. Write the equilibrium equation
Determine the reaction of the cable
Determine the tension of the cable
Compare this solution and the result of the Example 1 in the section 1 (slide 3).
38
Section 9

## Slide 107
Section 9 (continuation – 9.2)
Example 2. A weight G is suspended by a thread of the length l from a fixed point 0. It represents a conical pendulum as it traces a circular path on a horizontal plane. The thread forms an angle with the vertical. Determine the velocity of the weight and the tension T in the thread.
1. We choose an object (weight).
2. Discard the constraint (cable) and replace it by reaction R.
3. Add a force of inertia
4. Write the equilibrium equation
x
y
From the first equation define the
reaction of the cable
Determine the tension of the cable
Substitute the reaction of the cable and the force of
Inertia in the second equation and determine the velocity
of the load
■ D'Alembert's Principle for a System
D'Alembert's principle for a single particle k is
Having summed such equations for all the particles of a system we obtain
where Pk – resultant of the active forces applied to the particle k,
Rk – resultant of the reactions of constraints,
Fkin = - mak – force of inertia of the particle k.
Here P – principal vector of the active forces applied to the system (both external and internal),
R – principal vector of the reactive forces,
Fin– principal vector of the inertial forces of a system.
Thus, the geometric sum of principal vectors
of the given forces, reactions of constraints
and inertial forces of the particles equals zero.
Multiply the equation expressing the principle of d'Alembert by the radius vector drawn from the center O to the particle
Add all of n equations
Here MOP – principal moment of the active forces applied to the system with respect to the center O,
MOR– principal moment of the reactions with respect to the center O,
MOin– principal vector of the inertial forces of a system with respect to the center O.
Thus, the geometric sum of principal
moments of the given forces, reactions
of constraints and inertial forces of the
particles with respect to any center equals zero.
■ Reduction of the inertial forces of a rigid body to the simplest form
In dynamics the center of reduction is usually taken at the center of mass of a system. As a result, in general case we obtain the principal vector and principal moment of the inertial forces with respect to the center of mass
39
Compare this solution and the result of the Example 3 in the section 1 (slide 4).

## Slide 108
Section 9 (continuation – 9.3)
■ The principal vector of the forces of inertia for a body does not depend on the center of reduction and is equal to the product of the mass of the body and the acceleration of its center of mass, and is opposite in direction to the acceleration
■ Translational Motion. In this case, the inertia forces of a rigid body can be reduced to a single resultant through the center of mass
of the body. The principal moment with respect to the center of mass equals zero
The radius vector of the center of mass is zero if the center of reduction coincides with the center of mass.
■ Rotation about an Axis through the Centre of Mass. Let a body have a plane of symmetry, and let the axis of rotation Cz be normal to the plane through the center of mass.
In this case, the axis of rotation is the principal axis of inertia at O. Accelerations of all the particles lying on a straight line parallel to the axis of
rotation are geometrically equal. Therefore, the inertial forces of symmetrical particles relative to the plane of symmetry are also equal and their
resultant will lie in this plane (at the point Mk).
40
z
ω
ε
O
Mk
C
The principal vector of the inertial forces is
O
C
Mk
Acceleration of the center of mass equals
When we select the center of reduction at the point O, the principal vector of the inertial forces must be applied at this point, parallel
to the vector of the acceleration of the center of mass in the opposite direction.
At an arbitrary point Mк acceleration is
Since the line of action of the centrifugal forces of inertia passes through the center of rotation then
the principal moment of inertial forces is calculated as the sum of the moments of only rotational
forces of inertia
The principal moment of the forces of inertia is equal to the product of the angular
acceleration and the mass moment of the body about the axis of rotation, and is opposite in
direction to the acceleration
As we know, the system of any force and a couple can be replaced by a single force, resultant, applied at the new center of reduction. It can be
proved that the resultant of the inertial forces will be applied at the center of oscillation. Particularly, if the center of mass lies on the rotational
axis, the principal vector of the inertial forces equals zero and forces of inertia are reduced to the couple
Therefore, a system of inertia forces can be reduced to a principal vector and principal moment of these forces.

## Slide 109: Section 9 (continuation – 9.4)
■ Plane Motion. Let a body have a plane of symmetry, and let it be moving parallel to this plane. By virtue of symmetry, the
principal vector and the resultant couple of inertia forces lie, together with the center of mass C, in that plane.
41
xC
C
yC
zC
ε
In a plane motion a system of inertia forces can be reduced to a principle vector applied at the center of mass and a couple in the plane of symmetry of the body whose moment is equal to the principal moment of the inertia forces about the center of mass.
Example 3. The homogeneous rod OA of the mass M and length l, is pivotally suspended in a point O to z-axis. It rotates with an angular velocity
ω = const forming the angle  with the axis of rotation. Determine the forces of inertia and the angle .
ω
O
C
x
y
z
A

Inertia forces of the particles are proportional to the centripetal acceleration whose magnitude is in turn proportional to the distance of the particles to the axis of rotation (triangular distribution diagram).
Elementary inertial force applied to the elementary mass of the length ds, situated at a distance s from point O is
s
ds
dFin
By integrating along the length of the rod we obtain the principal vector of the inertia forces
The same result can be got much easier using the acceleration of the center of mass
The principal moment of the inertial forces can not be found by the formula Min0 = Ixx , because the rod OA is in a relative
equilibrium, and x =x = 0. However, the forces of inertia, due to the rotation of the rod relative to the z-axis, have a moment
Thus, the inertial forces are reduced to the principal vector
applied at the center of reduction O and principal moment
relative to this center.
The obtained system can be replaced by a force applied at the point, separated from the center of reduction along the perpendicular to the direction of the force at the distance
d
The angle  can be determined from the equation of the relative equilibrium
The resultant of the inertial forces is applied at the center of gravity of the distribution diagram of the inertia forces.
This arrangement corresponds to the center of oscillation.

## Slide 110
Differential equations of the plane motion of a rigid body =, =, .
D'Alembert's principle for a particle: if at any given moment to the active forces and the reactions of the constraints acting on a particle is added the inertia force, the resultant force system will be in equilibrium and all the equations of statics will apply to it.
D'Alembert's principle for a system: if at any moment of time to the effective external and internal forces acting on every particle of a system are added the respective inertia forces, the resultant force system will be in equilibrium and all the equations of statics will apply to it.
The principal vector of the inertia forces of a moving body is equal to the product of the mass of the body and the acceleration of its center of mass, and is opposite in direction to the acceleration.
In translational motion, the inertia forces of a rigid body can be reduced to a single resultant equal to the principal vector of the inertia forces applied at the center of mass of the body.
In rotational motion, a system of inertia forces can be reduced to a couple in the plane of symmetry of the body of the moment equal to the product of its mass moment with respect to the axis trough the center of mass perpendicular to the plane of symmetry and the angular acceleration.
In plane motion, a system of inertia forces can be reduced to the principal vector of the inertia forces applied at the center of mass of the body and a couple in the plane of symmetry of the body whose moment is a product of its mass moment with respect to the axis trough the center of mass perpendicular to the plane of symmetry and the angular acceleration.
42
Summary of Section 9

## Slide 111: Section 10
43
■ Analytical Mechanics
Analytical mechanics establishes common, uniform methods for studying the motion and balance of any complex material systems by means of mathematical analysis. For this purpose we introduce new concepts and summarize old.
■ Constraints are now considered as some conditions imposed on the system, which must be satisfied in the process of motion of the system. They contain the relations (equations or inequalities) between the coordinates, velocity and acceleration components, and possibly time.
Holonomic (geometric) constraints are expressed by the equations with respect to the coordinates or integrable differential equations for the coordinates
Nonholonomic (kinematic) constraints are expressed by nonintegrable differential equations relative to the coordinates,
i.e. equations containing not only the coordinates of the particles system, but also their derivatives with respect to time
Non integrability means that they can not be reduced to the form of equations of holonomic constraints.
Scleronomous (stationary) constraints do not depend on time. For example, the equation of the path obtained for a certain points of the connecting rod of a crank mechanism is considered as an equation of scleronomous holonomic constraint
Rheonomous (nonstationary) constraints depend on time. For example, the kinematic excitation of vibrations.
Bilateral constraints are described by the equation, excluding the possibility of leaving the point of the trajectory or the surface described by the equation. That corresponds, for example, to a rigid constraint of a hinged rod.
Unilateral constraints are expressed by the inequality regulating constraint in only one direction, for example, a flexible thread or smooth surface.
■ Generalized coordinates. The parameters of any dimensions describing the configuration of the system in space are called
generalized coordinates. Their first derivatives with respect to time are called generalized velocities and the second
derivatives are said to be generalized accelerations. We use the word "generalized" to emphasize the fact that such coordinates are
not necessarily of the type of the simple or systems and to indicate that they are not necessarily lengths or angles, but may be any
quantity appropriate to the description of the position of the system.
■ The number of degrees of freedom - the number of independent generalized coordinates through which we can express the Cartesian coordinates of all points of the system. For example:
A
x
y
yA
xA
O
Here, the position of any point of the rod (e.g., A) is uniquely determined by the value of only
one parameter, the angle , which is a generalized coordinate (q =  ). The number of degrees
of freedom is n = 1.The equation of the constraint for the considered point A is
If a system of N particles has m holonomic constraints, then the Cartesian coordinates may always be
expressed by the finite relations
The number of generalized coordinates equals n = 3N – m.

## Slide 112
Section 10 (continuation – 10.2)
■ Virtual Displacements
We shall define as a virtual displacement of a system the sum total of any arbitrary infinitesimal displacements of the particles of the system
consistent with all the constraints acting on the system at the given instant.
■ Actual displacements - infinitesimal (elementary) displacements, really (actually) occurring during the time dt,
permitted by imposed on the system constraints. Actual displacements depend on the forces applied to the system,
the type of constraints (stationary, non-stationary, holonomic, nonholonomic) and initial conditions. Thus, the virtual displacements are more general concept than the actual displacements.
Up to infinitesimal, the increments of the radius vector lie in the tangent plane to the surface of constraint and represent virtual displacements. In the case of non-stationary holonomic constraint f (x, y, z, t) = 0 virtual displacements are considered for the position and shape of the surface of the constraint corresponding to a given instant. Virtual displacements do not depend on the forces applied to the system.
s
ds
Since the location of the particle of a system can be expressed in terms of the generalized coordinates ,
the virtual displacements are expressed in terms of their increments as the total differential
or
■ Calculation of virtual displacements
Geometric method. Due to the smallness of virtual displacements of any particle , when turning, the particles displacements can be considered by moving along the perpendicular to the radius of rotation towards the angle of rotation
yA
xA
A
x
y
yA
xA
O
x
A
O
xA
yA=sA
For small angles cos ≈ 1, sin ≈ , hence,
For example, for an inclined rod
A
y
O
x
sA
Analytical method . The variation of coordinates are
Unlike the geometric method, the signs of coordinate
increments are obtained automatically. Using the geometric method, it is necessary to consider the direction of the obtained
increment (displacement).
44
■ The elementary work done by a force in any virtual displacement is called the virtual work.
In the coordinate form
In the natural form

## Slide 113
Section 10 (continuation – 10.3)
45
■ Examples
Example 1. Define the reaction of the right support.
A
B
a
l
The beam is fixed and has neither the capacity nor the actual displacements. Discard the constraint (moving pin joint) and replace it with the reaction.
Without the right support the beam can be rotated by the active forces, the reaction RB is considered as active force. Make a virtual displacement.
■ Ideal Constraints
Constraints, in which the sum of the virtual work produced by all the reaction forces in any virtual displacement of a system is zero, are called ideal constraints
If a particle has for a constraint a smooth surface, the reaction of the constraint is normal to the surface and the elementary work done by the force in any virtual displacement of the particle is zero. If we neglect rolling friction, the sum of the work done by the reaction forces and in any virtual displacement of a rolling body is also zero. The internal forces of any non-deformable system also possess this property.
■ The Principle of Virtual Works
The necessary and sufficient conditions for the equilibrium of a system subjected to ideal constraints is that the total virtual work done by all the active forces is equal to zero for any and all virtual displacements consistent with the constraints.
Proof of necessity. The system is in equilibrium and for each particle is satisfied the following equilibrium equation:
Multiply by the vector of the virtual displacement and add up
= 0
Proof of sufficiency. Given:
Assume that there is no equilibrium.
Each of the particles under the action of the active forces acquires, in time dt an actual displacement of dr. Considering these displacements as virtual, we calculate the work and adding up one obtains
= 0

sP
sB
Define the virtual work
Determine the virtual displacements
Example 2. Define the supporting moment of the left support in a multispan built-up beam.

sP
sB
Discard in a fixed support the constraint which opposes the turn of the beam and replace it with the moment MA.
MA
A
B
a
l
l
C
D
E
b
b
sD
Calculate the virtual displacements
Write the sum of virtual works

## Slide 114
Constraints are considered as some of the conditions imposed on the system, which must be satisfied in the process of motion of the system. They contain the equations between the coordinates, velocity and acceleration components, and possibly time.
Holonomic (geometric) constraints are expressed by the equations with respect to the coordinates or integrable differential equations for the coordinates.
Nonholonomic (kinematic) constraints are expressed by nonintegrable differential equations relative to the coordinates, i.e. equations containing not only the coordinates of the particles system, but also their derivatives with respect to time.
Scleronomous (stationary) constraints do not depend on time.
Rheonomous (nonstationary) constraints depend on time.
Bilateral constraints are described by the equation, excluding the possibility of leaving the point of the trajectory or the surface described by the equation.
Unilateral constraints are expressed by the inequality regulating constraint in only one direction.
We shall define as a virtual displacement of a system the sum total of any arbitrary infinitesimal displacements of the particles of the system consistent with all the constraints acting on the system at the given instant.
Constraints, in which the sum of the virtual work produced by all the reaction forces in any virtual displacement of a system is zero, are called ideal constraints.
The parameters of any dimensions describing the configuration of the system in space are called generalized coordinates. Their first derivatives with respect to time are called generalized velocities and the second derivatives are said to be generalized accelerations.
46
Principle of Virtual Works
The necessary and sufficient conditions for the equilibrium of a system subjected to ideal constraints is that the total virtual work done by all the active forces is equal to zero for any and all virtual displacements consistent with the constraints.
Summary of Section 10

## Slide 115: Section 11
47
■ The General Equation of Dynamics
The principle of virtual work gives a general method for solving problems of statics.
D'Alembert's principle makes it possible to employ the methods of statics in solving dynamical problems.
By combining both these principles we can develop a general method for the solution of problems of dynamics.
Sum over all points
= 0 for ideal constraints
We have obtained the general equation of dynamics
In a moving system with ideal constraints the total virtual work done by all the active forces and all the inertia forces in any virtual displacement is zero at any instant.
The shorter representation of the
general equation of dynamics is or
Or where A is the virtual work done by all the active forces and all the inertia forces in any virtual displacement.
Example. Centrifugal governor rotates around a vertical axis at a constant speed. At  = 0 the spring is not deformed. The stiffness of the spring is c.
The length of each rod is l. The arm of suspension is a. The weight of each of the balls is G, the clutch weight is . Determine the angular velocity of the steady rotation for a given angle .
a
1. We show the specified forces
2. Add the inertia forces
3. Elastic constraint (spring) which is not ideal (it does the work in the virtual displacements ) must be discarded and replaced by a reaction.
The module of the elastic force is proportional to the change of its length (shortening)
4. Define the projection of the virtual displacements
(variations of coordinates) of the force application points
A
B
x
y
5. Make the general equation of dynamics
Substituting the values of inertia forces
and the reaction of the spring we get
Hence, after some simplifications we obtain

## Slide 116
Section11 (continuation – 11.2)
■ Generalized Forces
Let the, for j be a set of generalized coordinates which uniquely specifies the instantaneous position of some dynamical system which has s degrees of freedom. Here, it is assumed that each ofcan vary independently.
48
The combination of these displacements is one of the virtual displacement of the system.
The elementary work of all the given forces in these displacements is
Give to some generalized coordinate qj an infinitesimal increment, leaving the rest of the generalized coordinates unchanged, i.e,
q1 = q2= … = qj-1= 0, qj ≠ 0, qj+1=…= qs= 0. As a result, all of the N points of the system will have some infinitesimal displacements
Put into correspondence to all the given forces of a system some imaginary force that makes the same work in this virtual (generalized) displacement qj that all forces of the system
Hence, the value of this force
is defined as
Thus, the generalized forces are coefficients of the increments of the generalized coordinates in the expression for the total elementary work of all forces applied to the system. It is obvious that the number of generalized forces is equal to the number of degrees of freedom.
1. The dimension of this force is determined by the dimension of the generalized coordinates. For example, if qj is a linear generalized coordinate, then the dimension of the generalized forces Qj corresponds to the force (N). If qj is the angular generalized coordinate, then the dimension of the generalized forces Qj corresponds to a couple or torque (Nm).
2. The number of generalized forces equals the number of generalized coordinates.
■ Other formulas for calculating the generalized force
In the vector form
The radius vector of the k-th point is a function of all generalized coordinates
The variation of the radius vector of generalized coordinates
at q1 =q2= … = qj-1= 0, qj ≠ 0, qj+1=…= qs= 0 is
Whence
In the coordinate form
In the case of potential forces

## Slide 117
Section 11 (continuation – 11.3)
■ Example of calculation of the generalized forces
For a mechanical system of three bodies with two fixed and one movable block determine generalized forces Qj .
49
1. The number of the generalized forces equals the number of generalized coordinates. The number of generalized coordinates is equal to the number of degrees of freedom, which can be defined by successive imposition of constraints. Restrict the horizontal displacement of the body 1, the bodies 2 and 3 can be moved vertically.
Restrict additionally the vertical displacement of the body 3.
Thus, n = 2. Select the generalized coordinates q1 = s1 and q2 = s2.
s1
s2
2. In order to determine Q1 consider an arbitrary small displacement q1 = s1 (q2 = s2=0).
s1
s1
s1/2
s1/2
Calculate the virtual work done by the effective forces in this displacement
3. In order to determine Q2 consider an arbitrary small displacement q2 = s2 (q1 = s1=0).
Calculate the virtual work done by the effective forces
s2
s2
s2/2
s2/2
The body 2 can not move.
Q1
Q2
■ Equilibrium Equations. According to the principle of virtual work at the equilibrium of a system
Consider the virtual displacements of the points of a system, caused by infinitesimal increments of generalized coordinates
Calculate the virtual work done by the effective forces
The increments of the generalized coordinates are arbitrary and independent of each other.
Therefore, in the obtained equation all coefficients
(generalized force) must be equal to zero
- equilibrium conditions.
In the above example, for the system to be in equilibrium it is necessary for the forces Q1 and Q2 to be zero. It is evident that Q1 ≠ 0 and there is no equilibrium. The equilibrium of the system is possible only when there is a certain value of the friction force between the body 1 and the plane. Then, this force will enter into the expression for Q1.
Now, the equilibrium equations for the system
define the relation between the forces and have the form

## Slide 118: Section 12
50
■ Lagrange’s Equations of Motion
Equations of Lagrange are differential equations of motion of a system with respect to generalized coordinates. We use the general equation of dynamics
where A is a virtual work of all the given forces and inertial forces in any virtual displacement.
1. We specify the virtual displacements of the particles of a system, caused by
infinitesimal increments of all generalized coordinates
Calculate the virtual work done by the given forces and inertial forces
Rearrange the sums or
of the products
Qj
Qjin
The increments of the generalized coordinates are arbitrary and independent on each other. Therefore, in the obtained equation all the coefficients
(generalized forces) must be equal to zero
- equations of motion equivalent to the general equation of dynamics.
2. The generalized inertia forces Qjin includes a mass and acceleration of the particles of a system. Express these forces through the kinetic energy
Add to this the expression two identical components of different signs and the following form :
Calculate the partial derivative of the kinetic
energy of a system with respect to generalized coordinate
Let us calculate the derivative in time of partial derivative of the kinetic energy with respect to the
generalized velocity
The derivative with respect to generalized velocity
has the similar expression
Therefore,
Substitute into equation of motion
Whence
- Lagrange’s Equations
For the conservative (potential) forces we get

## Slide 119
Section 12 (continuation – 12.2)
51
■ Kinetic potential is a function defined by the expression L = T – П - Lagrange’s function, where and
Kinetic potential is also a function of the generalized
coordinates, generalized velocity and time
Determine the kinetic energy through the kinetic potential as T = L + П and calculate the required partial derivatives involved
in the Lagrange’s equation
= 0, since it doesn’t depend on
or
a
2. Show the given forces.
3. Elastic constraint (spring) is replaced by the reaction. Include it into a
number of the given forces
4. Define the projections of the virtual displacements
(variation of coordinates) of the points of the force
application
A
B
x
y
5. Define the generalized force Q
6. Calculate the kinetic energy
Make up the
Equation of
Lagrange
Example 1. Centrifugal governor rotates around a vertical axis at a constant speed. At α= 0 the spring is not deformed. The stiffness of the spring is c.
The length of each rod is l. The shoulder suspension is a. The weight of each of the balls is G, the clutch weight is . Determine the angular velocity of the steady rotation for a given angle α.
The system has two degrees of freedom (rotation about the axis and the change in the angle α).
In a steady rotation consider only the change in angle α and select it as a generalized coordinate q = .
After substituting R we find 

## Slide 120
Section 12 (continuation – 12.3)
52
2. Generalized forces Q1, Q2
were calculated in Example:
3. Define kinetic energy of a system
Example 2. For a mechanical system of three loads with two fixed and one movable block determine accelerations of the loads.
The system has two degrees of freedom (see example calculation of the generalized forces, Section 11, slide 50).
Lagrange’s equations have the following form when selecting generalized coordinates q1 = s1 and q2 = s2:
s2
s1
4. Calculate the partial derivatives of the kinetic energy
5. Calculate the derivatives
with respect to time
6. Substitute the obtained expressions and the generalized forces in Lagrange’s equations
Or
Unknown (independent) accelerations are
In the case of equal masses M1=M3=M,
we get

## Slide 121
Section 12 (continuation – 12.4)
53
■ Equilibrium Equations in Generalized Coordinates
By definition, the generalized force for a conservative system is
Hence, it follows that equilibrium position (rest) of a conservative system corresponds to the extreme values of the potential energy of a system.
In this case, from the vanishing of the partial derivative of potential energy, the stability of a state of equilibrium can not be concluded.
The stability condition of a state of rest can be established by criterion of Lagrange-Dirichlet :
The position of equilibrium of a conservative system, in which the potential energy reaches a minimum, is a stable state of equilibrium.
- condition of the minimum of potential energy.
If the second derivative of the potential energy is less than zero, this corresponds to the case of unstable equilibrium. If the second derivative of the potential energy equal to zero, then this cannot serve as a criterion of a minimum of the potential energy and the solution of the question about the stability of equilibrium is necessary to examine by defining the signs of the derivatives of a higher order. If the first non zero derivative of the potential energy, has even order and is greater than zero, this corresponds to the minimum of potential energy
(the equilibrium position is stable).
If the first non zero derivative of the potential energy is of odd order, the potential energy has not extremum (no minimum or maximum).
It corresponds to the neutral equilibrium.
Example. The metronome is a pendulum with two weights: A - fixed weighing GA , B – movable, of the weight GB. Determine the conditions of stable and unstable equilibrium position.
A
B
LA
LB
x
y
Choose as the generalized coordinate the angle of deviation of the shaft from the vertical φ.
φ
The potential energy of the system is
The equilibrium condition is
Analyze the stability of equilibrium of the system
under conditions (a) and (b).
In the case of (a), GALA=GBLB, the second derivative, as all subsequent vanishes. This corresponds to the neutral equilibrium.
If GALA>GBLB and φ =0 the second derivative is greater than zero and this corresponds to a stable equilibrium .
If GALA>GBLB and φ =180о the second derivative is less than zero and this corresponds to an unstable equilibrium.

## Slide 122
In a moving system with ideal constraints the total virtual work done by all the active forces and all the inertia forces in any virtual displacement is zero at any instant.
The generalized forces are coefficients of the increments of the generalized coordinates in the expression for the total elementary work of all the forces applied to the system. It is obvious that the number of generalized forces is equal to the number of degrees of freedom.
A holonomic system with perfect constraints is in its equilibrium only if all generalized forces corresponding to generalized coordinates are equal to zero.
Lagrange’s equations .
Kinetic potential is a function defined by the expression L = T – П - Lagrange’s function.
Another form of Lagrange’s equations 0.
The position of equilibrium of a conservative system, in which the potential energy reaches a minimum, is a stable state of equilibrium.
If the second derivative of the potential energy is less than zero, it corresponds to the case of unstable equilibrium.
The equilibrium position (rest) of a conservative system corresponds to the extreme values of the potential energy of a system.
54
If the second derivative of the potential energy equal to zero, then the stability of equilibrium is necessary to examine by defining the signs of the derivatives of a higher order.
Summary of Sections 11-12
If the first non zero derivative of the potential energy has even order and is greater than zero, the equilibrium position is stable.
If the first non zero derivative of the potential energy is of odd order, the potential energy has not extremum (no minimum or maximum). It corresponds to the neutral equilibrium.

## Slide 123
55

## Slide 124
God, bless mechanics!
56