ТМ-9 part 1

Determine laws of motion of bodies 2 and 3 (fig. 1), absolute velocity and acceleration of point М. It is known, that the law of motion of body 1 is x1 = 5t2, m; external radius of body 2 is R2 = 1 m, internal radius of body 2 is r2 = 0.5 m, and a radius of body 3 is R3 = 0.75 m, time parameter is t = 1 s.

Fig. 1 Initial scheme

Solution

| Given: x1 = 5t2, m R2 = 1 m r2 = 0.5 m R3 = 0.75 m t = 1 s Find: φ2, φ3, vM, aM |  |
| --- | --- |
|  | Fig. 2 Calculation scheme |

Construct a calculation scheme (fig. 2). Place additional points A, B, C, D, P on it, and directions of motion of bodies 2 and 3, directions of angular velocity ω3 and angular acceleration ε3 of body 3, and a vector of absolute velocity vM.

Body 1 moves linearly, body 2 rotates, and body 3 performs plane motion. Body 1 and point A are connected through an ideal string (the one that doesn’t deform). Points B and D, P and a support are also connected through an ideal string.

Direction of motion of body 1 is given in the initial data. If body 1 moves linearly along an inclined surface and is connected with point A through an ideal string, then body 2 rotates clockwise (designated as φ2 in fig. 2). Direction of motion of body 3 can be determined analogically. Body 3 rotates counterclockwise (designated as φ3 in fig. 2).

If a string is ideal, then movement of body 1 is equal to a length of a string, which is wound up on external radius of body 2. Analogically, a length of a string, which is unwound from internal radius of body 2, is equal to a length of a string, which is wound up on radius of body 3. Express string lengths using the angle and radius of rotation.

Determine the equations of kinematic connections

,

.

From where the laws of motion of bodies 2 and 3 are

,

.

Determine angular velocity ω3 and angular acceleration ε3 of body 3.

,

.

ω3 and ε3 are directed counterclockwise since they are positive for a positive t.

Body 3 performs plane motion and is connected with a support through a string. Then a center of rotation (instantaneous center of velocity) of body 3 is point Р.

Determine absolute velocity of point М.

.

At the moment of time t = 1 s

.

Absolute acceleration of a body, which performs plane motion, is determined as a vector sum of accelerations of a pole , normal , and tangent  accelerations of the considered point around this pole. The pole is the point, acceleration of which is known or is easy to calculate. Define point С as a pole since it is a center of mass of body 3 and moves linearly.

Determine acceleration of point С

,

,

.

Determine normal and tangent accelerations of point М relatively to the pole С at the moment of time t = 1 s

,

.

In order to determine absolute acceleration of point М, project the vectors of determined accelerations on coordinate axes x and y (fig. 3). Note that normal acceleration  is directed from point M to the pole C, and tangent acceleration  is perpendicular to the normal acceleration and is directed along angular acceleration .

Fig. 3 Acceleration calculation scheme

Then absolute acceleration aM of point М

Answer: , , , .